## Slide 1: 4 Cache Memory Optimization (Part 1)
Peter H. Chen

## Slide 2: 4 Cache Memory Optimization (Part 1)
Cache Memory Optimization (Part 1) (00:32/38:34))
00:31 Last week and this week our lecture videos are focusing on optimization of cache memories.
00:38 Optimization concept is basically used to improve the performance of cache memory by
00:45 reducing average memory access time.
00:47 Today we will have a little deeper investigation on few cache memory optimization problems.
https://nptel.ac.in/courses/106103183

## Slide 3: 4.1 Problem 1: Block Size from Address

## Slide 4: 4.1 Problem 1: Block Size from Address
Cache Memory Optimization (Part 1) (00:32/38:34))
00:55 Let us move to the first problem.
00:59 The address of a word in a byte addressable 16 MB physical memory is 0xAA0C2A.
https://nptel.ac.in/courses/106103183

## Slide 5: 4.1 Problem 1: Block Size from Address
Cache Memory Optimization (Part 1) (00:32/38:34)
01:06 So this is represented in hexadecimal form.
01:09 This is the address it is a 16 MB physical memory.
01:14 So when you have 16 MB the total address space is of 24 bit.
01:18 This is the 24-bit address represented in hexadecimal form.
01:22 This word upon bringing to cache is mapped to set number 48.
01:28 What is the block size of the cache memory?
01:30 So we do not know anything about what is the size of the cache memory.
01:34 Only thing is this particular address upon bringing to cache was mapped to set number
01:40 48.
01:42 Let us try to see how this is getting solved.
01:44 So this is the hexadecimal address that is given, when a convert it into binary form.
01:49 A stands for 1010, this is what you see here.
01:52 Second A is 1010, 0 is 0000, C is 1100, 2 is 0010 and again A is 1010.
https://nptel.ac.in/courses/106103183
24 bits = 2^4 * 1 MB = 16 MB
0xAA0C2A = 24 bits
AA0C2A
= A A 0 C 2 A
= 1010 1010 0000 1100 0010 1010
= 101010100000110000101010

## Slide 6: 4.1 Problem 1: Block Size from Address
Cache Memory Optimization (Part 1) (00:32/38:34)
02:01 This is what we have.
02:03 Now we know that in the case of a general splitting up of cache memory address, we have
02:10 the index portion, we have an offset portion, we have a tag portion.
02:13 So somewhere few middle bits will tell you which is the set number to which this address
02:19 is mapped.
02:21 We have already it this mentioned in the question that we are going to mapped this into set
02:26 number 48.
02:27 So somewhere here we should get an address such that the value is 48.
02:32 And you know that 48 is obtained by 32 + 16.
02:36 So, when you look at this, the same address you can see that whatever is marked in red
02:46 110000, that constitute to set number 48.
02:50 So, if that is going to be the set number, whatever is balance should be the offset.
02:55 Because, the organization in which the address is split is tag bits followed by index bits
https://nptel.ac.in/courses/106103183
Tag bit
index bit
Offset bit

## Slide 7: 4.1 Problem 1: Block Size from Address
Cache Memory Optimization (Part 1) (00:32/38:34)
03:00 followed by offset bits.
03:01 Now, in this case we have to assume this is your tag, this is your index and this is your
03:06 offset.
03:07 Since you have 6 more bits, after the index bit your offset is and that is what is called
03:12 64 bytes.
https://nptel.ac.in/courses/106103183
Offset bit = 2 ^ 6 = 64 bytes

## Slide 8: 4.1 Problem 1: Block Size from Address
Cache Memory Optimization (Part 1) (00:32/38:34)
03:13 So, in this kind of questions what we do is once you get the address. From the address
03:18 you look for a pattern, here we should get a number called 48. (index)
03:24 And 48 is obtained by 32 + 16, they are adjacent powers of 2.
03:28 So, we should have 110000.
03:31 Look for that pattern and whatever that pattern is there; that means, the set number portion
03:37 is identified.
03:38 Once you have identified the set number portion everything towards the left side is your tag,
03:42 everything towards your right side is offset and with that we can find out what is the
03:46 block size; so, moving onto the second problem.
https://nptel.ac.in/courses/106103183
Offset bit = 2 ^ 6 = 64 bytes
(110000)₂ = (1 × 2⁵) + (1 × 2⁴) + (0 × 2³) + (0 × 2²) + (0 × 2¹) + (0 × 2⁰) = (48)₁₀

## Slide 9: 4.2 Problem 2: Better Performance

## Slide 10: 4.2 Problem 2: Better Performance
Cache Memory Optimization (Part 1) (00:32/38:34)
03:51 A cache has an access time of hit latency 10 ns and the miss rate of 5 %. An optimization
03:58 was done so as to reduce the miss rate to 3%.
04:02 But the hit latency was increased to 15 ns.
04:06 So, here we have a scenario; where a cache miss rate was reduced, but the hit latency
04:13 was increased.
https://nptel.ac.in/courses/106103183

## Slide 11: 4.2 Problem 2: Better Performance
Cache Memory Optimization (Part 1) (00:32/38:34)
04:15 We know that average memory access time is defined by; Hit time + Miss rate x Miss penalty.
04:22 Under these circumstances, the question is all about whether this optimization will improve
04:28 cache performance or not.
04:30 Now we will see average memory access time of the first case that is prior to optimization
04:35 is defined as hit time plus miss rate into miss penalty and we know hit time is equal
04:40 to 10 nanosecond.
https://nptel.ac.in/courses/106103183
AMAT 2 = 15 + 0.03 x ? = 15 + ?
AMAT 1 = 10 + 0.05 x ? = 10 + ?

## Slide 12: 4.2 Problem 2: Better Performance
Cache Memory Optimization (Part 1) (00:32/38:34)
04:41 And miss rate is equal to 0.05 because, it is already been given miss rate is 5 percent.
04:48 So, miss rate is 0.05.
04:49 The second case average memory access time of the optimization is defined as the new
04:56 hit time.
04:57 That is 15 nanosecond plus the new miss rate miss rate is 0.03 into (x) the miss penalty.
https://nptel.ac.in/courses/106103183

## Slide 13: 4.3 Problem 3
Cache Memory Optimization (Part 1) (00:32/38:34)
05:04 Now, if you wanted to say that the optimization has improved the performance, then average
05:10 memory access time of the second case should be less than average memory access time of
05:17 the first one.
https://nptel.ac.in/courses/106103183

## Slide 14: 4.3 Problem 3
Cache Memory Optimization (Part 1) (00:32/38:34)
05:18 So, how will you solve this?
05:20 So, if you are going to write it as average memory access time of 2 that is 15 nanosecond,
05:26 plus 0.03 into(x) the miss penalty let us say we call it as M should be less than 10
05:35 plus 0.05 M. If you try to solve this, you get as 15 minus 10 that is going to be 5 should
05:48 be less than 0.02 M. So, this is the inequality that you are going
05:55 to get.
05:56 So, M value should be it indicates that the miss penalty value should be greater than
6:05 250 nanosecond.
https://nptel.ac.in/courses/106103183

## Slide 15: 4 Cache Memory Optimization (Part 1)
Cache Memory Optimization (Part 1) (00:32/38:34)
06:07 So, only under this context we can say that the average memory access time of the optimized
06:14 cache is lower than the average memory access time to prior to optimization case.
06:23 To summarize this problem, we have given two scenarios.
06:27 Cache number one has certain specific hit time and miss rate.
06:31 Second cache has different hit and hit rate.
06:34 And, the question is when can we say that second cache memory is better than the first
06:38 cache memory.
06:39 Performance of cache memory is basically as such using average memory access time which
06:43 is hit time plus miss rate into miss penalty.
06:45 So, we try to find out an inequality which tells average memory access time of the second
06:51 cache is lower than the average memory access time of the first cache.
06:54 Upon solving we get a value for miss penalty.
06:58 So, the optimization will work if and only if the miss penalty is larger than 250 nanosecond.
07:04So, that concludes problem number 2.
https://nptel.ac.in/courses/106103183

## Slide 16: 4.3 Problem 3

## Slide 17: 4.3 Problem 3)
Cache Memory Optimization (Part 1) (00:32/38:34)
07:06 Now, we move onto problem number 3 if you look at problem number 3 we can see that cache
07:12 as a hit rate of 90 percent 64-byte block.
07:18 Cache hit latency of 5 nanosecond.
07:22 Main memory takes 150 nanosecond to return the first word.
07:25 And here the word length is given as 32 bits and 10 nanosecond for each subsequent word.
07:31 So, the question has 2 components, what is the miss latency of the cache ok?
07:36 So, if you look at what is miss latency of the cache, first we have to find out.
07:41 So, here the miss latency is not given, some indications are given to compute it , where
07:46 it takes 150 nanosecond to return the first word and 10 nanoseconds each for each subsequent
07:52 word.
07:53 We know that in the case of a cache memory we have a block concept, when you go to the
07:57 next level mainly to the main memory we are going to bring a block of data.
https://nptel.ac.in/courses/106103183

## Slide 18: 4.3 Problem 3
Cache Memory Optimization (Part 1) (00:32/38:34)
08:01 And this block of data cannot be brought in a single clock cycle.
08:05 So, it takes some amount of time to identify the first word and transfer it.
08:10 Then it is word by word you are going to transfer.
08:13 In the question it is mentioned that the first word is going to take 150 nanosecond, each
08:19 subsequent word is going to take another 10 nanosecond each.
08:23 Let us now find out what is the number of words per block.
08:30 So, when you look at the number of words per block, your block size is 64 bytes, and one
08:38 word is actually 4 byte because, 32 bit is being given as a word length.
08:44 So, this shows that you can accommodate 16 words inside a block.
08:49 Now if we look into the miss penalty component, out of the 16 word the first word is going
08:56 to take 150 nanosecond.
08:59 Now you have another 15 more words, each of this 15 word will take 10 nanosecond each.
https://nptel.ac.in/courses/106103183

## Slide 19: 4 Cache Memory Optimization (Part 1)
Cache Memory Optimization (Part 1) (00:32/38:34)
09:04 So, your miss penalty component is actually 300 nanosecond.
09:10 So, what is the miss latency of the cache that is the question that is mentioned.
09:15 So, we are going to find out what is the miss penalty or miss latency.
09:21 And this miss latency is depend on number of words that you have.
09:25 You have to find out the number of words, your block size is 64 bytes, one word is 4
09:30 byte.
09:31 So, 64 byte divided by 4 byte, you will be getting 16 words.
09:36 Now in the 16 words first word will take 150 nanosecond.
09:40 Each subsequent word will take 10 nanosecond each which makes 150 plus 15 into 10 that
09:47 is 300 nanosecond.
09:48 Let us see: what is the average memory access time in this case.
09:52 It is hit time so; the value of hit time is 5 nanosecond.
09:59 Plus, the miss rate is 90 percent is the hit rate.
https://nptel.ac.in/courses/106103183

## Slide 20: End