## Slide 1: 3 Basic Cache Optimization (Part 1)
Peter H. Chen

## Slide 2: 3 Basic Cache Optimization
Basic Cache Optimization (00:45/43:50)
How to improve the performance of Cache Memory?
Cache Memory is used to store the frequently used data.
The process during its instruction of pipeline requires accessing of cache memory to fetch the instructions.
…and if it is a load or a store instruction, then it will access for data as well.
How fast your cache can respond back is one important parameters, which will governs the performance of the pipeline as well.
In short, cache memory has a very significant role to play with respect to the performance of any instruction pipeline as well.
Today, we will focus our attention on a class of techniques, know as cache memory optimization techniques.
https://nptel.ac.in/courses/106103183

## Slide 3: 3 Basic Cache Optimization
Basic Cache Optimization (01:38/43:50)
So, we will focus about six cache optimization today.
And the idea of an optimization is there are various parameters that impacts the performance of cache,
…how can you fine tune these parameters such that overall accessing the memory is going to be faster than conventional mechanisms.
So, basic cache optimization techniques, accessing cache memory; we know that cache memory is acting as an interface between your CPU and the memory.
So, when CPU is there and the main memory is there, we have a high speed device which is called cache memory that is interacting with both CPU as well as your main memory.
So, you can have scenario such that whatever is the requested address is already present in the cache and that scenario is known as cache hit.
We call this time required to perform an access on a cache and return the accessed word is known as Hit Time.
https://nptel.ac.in/courses/106103183

## Slide 4: 3 Basic Cache Optimization
Basic Cache Optimization (02:32/43:50)
We call this time required to perform an access on a cache and return the accessed word is known as Hit Time.
There can be certain cases where the requested address may not be present in the cache memory.
We call such kind of scenarios as cache memory misses.
And the extra amount of time required to go to the next level of memory, in this case it is a main memory; extra amount of time required to go to the next level of memory, bring a block of data and put it in the cache memory that is known as miss penalty.
So, we have scenario where we are going to have hits in the cache and the time for accessing, a word in the cache and responding back to CPU if it is a hit, it is known as hit time.
https://nptel.ac.in/courses/106103183

## Slide 5: 3 Basic Cache Optimization
Basic Cache Optimization (03:29/43:50)
And the time to respond back with a block of data from an upper level memory to the cache memory, once we identify it is a miss it is known as miss penalty.
The average memory access time for any memory hierarchy consisting of a cache is defined as AMAT, Average Memory Access Time, is equal to hit time plus miss rate into (x) miss penalty.
Let us see, what is the aspect of hit time; when CPU gives an address, it may or may not be present in the cache, whether it is present in the cache or whether it is not present in the cache, we have to perform an indexing.
That means, you go into the appropriate index and then perform a tag comparison.
Then only we will come to know whether it is a hit or a miss; if it is a hit, we are returning with the requested word; if it is a miss, then the miss penalty starts you go to the next level of memory bring a block of data and then you return the word.
So, whether or not it is a hit or a miss, hit time will always be there for every memory access.
https://nptel.ac.in/courses/106103183

## Slide 6: 3 Basic Cache Optimization
Basic Cache Optimization (04:33/43:50)
We call this time required to perform an access on a cache and return the accessed word is.
So, there are certain memory access which maybe miss, it maybe cache miss.
So, the amount of time it is a cache miss that is call miss rate into(x) the miss penalty, the number of cycles.
So, in all the cases there will be hits, in some cases there will be miss and the miss
penalty will be computed in those cases in order to compute average memory access time.
What do you mean by hit time?
Time to find the block in the cache and return it to the processor, it involves indexing time, tag comparison and transfer of data.
Second one is known as miss rate.
It is a fraction of time the cache access is resulting in a miss, number of cache access that resulted in a miss divided by number of access to be cache.
https://nptel.ac.in/courses/106103183

## Slide 7: 3 Basic Cache Optimization
Basic Cache Optimization (05:19/43:50)
Miss penalty is number of additional cycles is very important, number of additional cycles required upon encountering a miss to fetch a block from the next level of memory hierarchy.
So, these are the three important terms.
So, we have to understand that your average memory access time is dependent or not, how much time it is required to access your first level of cache for your cache memory, for say effectively it is the indexing time, the tag comparison time and the transfer time.
Second important parameter that governs average memory access time is the miss rate; lower the miss rate, lower will be the average memory access time. And third parameter is called the miss penalty.
https://nptel.ac.in/courses/106103183

## Slide 8: 3 Basic Cache Optimization
Basic Cache Optimization (06:03/43:50)
Then how to optimize a cache, optimization of cache means you have to reduce average memory access time.
And AMAT (Average Memory Access Time) is defined by the equation of hit time plus miss rate into (x) miss penalty.
So, there are three basic motives by which we can reduce the average memory access time.
So, the first thing is you try to come up with the techniques which will reduce the miss rate that is called reduction of miss rate.
Second technique is try to come up with techniques that can reduce the miss penalty.
And the third technique is trying to reduce the hit time, but we have to understand that these three parameters are not independent; if you try to adjust one of this parameter, it will automatically impact the other parameter.
So, altogether changing one parameter is not an independent scenario, we may have to adjust or we may have to see what happens to the other parameters as well.
https://nptel.ac.in/courses/106103183

## Slide 9: 3 Basic Cache Optimization
Basic Cache Optimization (06:53/43:50)
Let us see the first optimization; the first optimization that is done to improve average memory access time is to increase the block size of the underline cache memory.
So, whenever we go for larger block size, we are able to reduce the miss rate.
So, miss rate is a parameter which we going to focus our attention now miss rate.
Now how this happens, the advantages of going for larger block is we are trying to utilize spatial locality.
https://nptel.ac.in/courses/106103183

## Slide 10: 3 Basic Cache Optimization
Basic Cache Optimization (07:25/43:50)
Assume you have a block which consists of a 8 words.
So, whenever CPU gives an address, you are going in searching in the cache;
the moment you come to know it is a miss, you are going into main memory bringing 8 word block together.
So, if there is strict spatial locality for your programs, let us say the access is to the remaining 7 words in the block, since I bring 8 words together the subsequent 7 words will always be a hit.
Now, if you assume that your block size is doubled, your block can accommodate 16 words.
https://nptel.ac.in/courses/106103183

## Slide 11: 3 Basic Cache Optimization
Basic Cache Optimization (08:00/43:50)
So, once we encounter a miss 16 were words are brought; that means, if we are going to have sequential access the remaining 15 of them will be a miss.
So, we have one miss and remaining 15 of them will be hit.
If we have 32 words in a block, remaining 31 will be hits, so that means we are able to have more number of hits for one block period, but this cannot be made very large certain point; beyond certain point of time your programs may not exhibits spatial locality at this point larger block sizes are really counterproductive.
https://nptel.ac.in/courses/106103183

## Slide 12: 3 Basic Cache Optimization
Basic Cache Optimization (08:38/43:50)
Second one this is though, the point that we address just now is called reduction of miss and what are one of these category of miss these are all compulsory miss.
We have seen in our last lecture that there are three different types of misses.
The first one is called compulsory miss, the misses that are encountered on the very first access of a block.
Second one is the capacity miss, which is happening due to smaller cache sizes.
And the third one is conflict miss which happens when two addresses are mapping into the same block.
https://nptel.ac.in/courses/106103183

## Slide 13: 3 Basic Cache Optimization
Basic Cache Optimization (09:06/43:50)
Now, how are we able to reduce the compulsory miss in this context; by virtue of the definition of compulsory miss, it is a very first miss that happens on a block.
So, when you have a larger block, you are going to miss only at the beginning of a block and all other subsequent request are going to be hit.
So, when you increase block size, you are able to reduce compulsory miss.
https://nptel.ac.in/courses/106103183

## Slide 14: 3 Basic Cache Optimization
Basic Cache Optimization (09:32/43:50)
Now, I told every parameter fine tuning is automatically going to affect the other parameter.
We will see; what are the draw backs of increasing block size.
First one this increases miss penalty, so how is this point addressed;
9:45 consider the case of an example where you have a block and this block is having assume 4 words can be accommodated, and the second design is you have a block where you have 8 words.
Now in both these cases you are having a main memory, now to the main memory we are going to connect using a bus.
https://nptel.ac.in/courses/106103183

## Slide 15: 3 Basic Cache Optimization
Basic Cache Optimization (10:00/43:50)
Now in both these cases you are having a main memory, now to the main memory we are going to connect using a bus.
Let us assume in the case of 4 words; if the carrying capacity of the bus is also 4 words.
Then in one clock cycle, I can bring 4 words together whereas, when I increase my block size to 8; the capacity of the channel that connects the cache memory and the main memory is not changing.
So, we require one 4 words will go in single stretch, the next 4 words is going to come in the next clock cycle only, that is the next memory cycle only.
So, when you increase the block size with the bandwidth connecting cache and memory unaltered then more number of memory cycles are required in order to carry this, this will effectively increase the miss penalty.
https://nptel.ac.in/courses/106103183

## Slide 16: End