## Slide 1: 4 Cache Memory Optimization (Part 3)
Peter H. Chen

## Slide 2: 4.6 Problem 6

## Slide 3: 4.6 Problem 6
Cache Memory Optimization (Part 3) (00:32/40:09)
30:04 This is the data; you are going to bring 8 words.
30:07 So, let us look into the data last 5 portion, F5F8.
30:14 F is 1111, 5 is 01 01, 1111, 8 is 1000.
30:24 Now let us try to extract these 10 bits.
30:31 These are 10 bits 1 10101 followed by 4 more ones.
30:38 And this indicates the value 863.
30:41 So, set number 863 can actually accommodate 4 words, but this is not starting from the
30:48 beginning if you do the split up again.
https://nptel.ac.in/courses/106103183

## Slide 4: 4.6 Problem 6
Cache Memory Optimization (Part 3) (00:32/40:09)
30:52 This is actually word number 2.
30:54 So, you have total of 4 words word 0, whose offset will be 00, these 2 bits, then 01 will
31:03 be word number 1, 10 is word number 2 and 11 is word number 3.
31:07 So, since split up is like this; that means, in 863 even though I bring 4 words, only two
31:13 words, word number 3 and word number 4 is of my interest so, 863 have only two words.
31:20 864 will have next four words and 865 also I bring four words out of which it contains
31:29 my two more words.
https://nptel.ac.in/courses/106103183

## Slide 5: 4.6 Problem 6
Cache Memory Optimization (Part 3) (00:32/40:09)
31:31 So, that data which is located from this address upon bringing to cache, it will occupy set
31:38 number 863, 864 and 865.
31:40 So, these are the set numbers in the L1 cache that are filled upon bringing this instruction
31:48 and data.
31:49 So, the idea is simple once you get the split up of the L1 cache like tag, index and offset,
31:55 find out the index bit, find out what is the corresponding decimal value of this index
https://nptel.ac.in/courses/106103183

## Slide 6: 4 Cache Memory Optimization (Part 3)
Cache Memory Optimization (Part 3) (00:32/40:09)
32:01 bit.
32:02 Here we have a 10-bit index.
32:03 So, go to that now let us see how will be solved for this L2 cache.
32:09 First let us write down what is the spilt up that is used in the case of an L2 cache.
32:16 So, we have a 12 bit tag and 11-bit index and a 5 bit offset that makes it total 28.
32:26 So, the same line like 8226620, if you write 6620 alone.
32:35 So, you have a 12-bit tag 6620, 01100110, 2 stands for 0 0 1 0 and this is 0.
32:45 So, this is 8226620.h Now, I am going to extract my 11 bits.
32:55 So, this is the 11 bit that we are talking about.
https://nptel.ac.in/courses/106103183

## Slide 7: 4 Cache Memory Optimization (Part 3)
Cache Memory Optimization (Part 3) (00:32/40:09)
33:04 So, 01100110001, and this value is 817.
33:11 Since the offset is fully 0, 817 can accommodate 8 words because, you going to see that your
33:18 L2 cache can accommodate 8 words.
33:21 And 818 will accommodate the next 8 words.
33:25 So, set number 817 and 818 of the L2 cache will occupy the 16 instruction words that
33:33 is being given part of this program.
https://nptel.ac.in/courses/106103183
8 words

## Slide 8: 4 Cache Memory Optimization (Part 3)
Cache Memory Optimization (Part 3) (00:32/40:09)
33:35 Now, if you look at the data portion the data address.
33:39 So, if you write F5F8F5, F is 1 1 1 1 and 8 is 1 0 0 0.
33:51 Now we are going to extract 11 bits of this.
33:56 So, the 11-bit value is 1 1 1 1, 0 1 0 1, 1 1 1 this the numerical equivalent of this
https://nptel.ac.in/courses/106103183

## Slide 9: 4 Cache Memory Optimization (Part 3)
Cache Memory Optimization (Part 3) (00:32/40:09)
34:07 is 1967.
34:08 So, set number 1967 can accommodate 8 words.
34:13 Now, you see how many words can be stored here.
34:18 It is actually telling that this is belonging to word number 6.
34:22 So, only two words can be accommodated in this block.
34:25 Even though I bring 8 words only two words word number 6 and word number 7 belongs to
34:32 this program.
34:33 So, the next one is 1968, that will bring another eight more words.
34:39 So, that contains your remaining six.
34:41 So, 1967 if will have two words of our program, and 1968 will have another six words of our
34:50 program.
https://nptel.ac.in/courses/106103183

## Slide 10: 4 Cache Memory Optimization (Part 3)
Cache Memory Optimization (Part 3) (00:32/40:09)
34:51 So, here also the concept is simple we have the split up 12-bit tag 11-bit index and remaining
34:56 5 bit offset from the given address find out the set number.
34:59 And from the offset you come to know whether this particular words are been filled from
35:03 the beginning of the offset or somewhere in between.
35:07 And once if it is full it is always going to the adjacent set number.
https://nptel.ac.in/courses/106103183

## Slide 11: 4 Cache Memory Optimization (Part 3)
Cache Memory Optimization (Part 3) (00:32/40:09)
35:11 So, to conclude we know that for L1 cache set number 610, 611, 612 and 613.
35:19 These carry four words see we have total of four sets.
35:22 And so, your sixteen instructions are located in set number 610, 11, 12 and 13; each of
35:29 the set has four words.
35:30 And your data is located in set number 863 which has two of your words.
35:35 Even though it has four words only two words is relevant to you.
35:40 864 has six words and 865 has another two words.
35:44 So, eight words, eight data words of the belong into array A is located in set numbers 863,
35:49 864 and 865.
35:50 And for L2 cache we can see that it is set numbers 817 and 818 that are been used.
35:58 And sets 1967 and 1968 is with the unused or the one that are filled in the L2 cache.
https://nptel.ac.in/courses/106103183

## Slide 12: 4 Cache Memory Optimization (Part 3)
Cache Memory Optimization (Part 3) (00:32/40:09)
36:07 So, these problem give a comprehensive treatment on when you move data and instruction across
36:14 cache hierarchy; which are the set number that are getting affected.
36:17 So, the basic concept is simple.
36:19 Once you have the main memory addressability, you know: what is the number of bits in the
36:25 address.
36:26 Find out the number of sets in the cache with the equation cache size divided by block size
36:32 into associativity.
36:33 Once you get the set numbers, you can find out what is the number of bits in the tag,
36:37 number of bits in the index and number of bits in the offset.
36:41 Once you get this from the given address whatever be the address the physical address that is
36:45 given from the physical address, you go and extract the index bits.
36:50 That will tell you which of the set number is getting affected.
36:53 So, with this we are coming to the end of this tutorial also.
36:58 There was last tutorial which was floated on week number 2 which gave about primitive
https://nptel.ac.in/courses/106103183

## Slide 13: 4 Cache Memory Optimization (Part 3)
Cache Memory Optimization (Part 3) (00:32/40:09)
37:05 concepts in cache memory.
37:07 And this tutorial is giving a in depth treatment or optimization and the mapping in cache memory.
37:14 There are many other problems that are also solved in part of the textbook.
37:19 All these problems you can get from the Hennessy and Patterson textbook of computer architecture.
37:24 This already mentioned in lecture 0 what is the text book that we are following.
37:29 Hennessy and Patterson textbook will help us in going through this concept of cache.
37:35 Practice will familiarize with as many number of questions.
37:38 I hope the assignment questions that are posted on our course website.
37:43 It will give you some kind of an understanding about how to work with cache memories.
37:49 So, with respect to this course, the first component that is storage aspect cache memory
37:54 we have almost now covered into 4 weeks.
37:59 And I hope these tutorial sessions are really useful for you in understanding cache memory
38:04 concepts in depth.
38:06 We will see you in the next week with DRAM structures.
38:18 Thank you.
https://nptel.ac.in/courses/106103183

## Slide 14: End