## Slide 1: 1 HPC Multi-Core Design by Gem5 (Part 2)
Peter H. Chen

## Slide 2: 1 HPC Multi-Core Design by Gem5 (Part 2)
HPC Multi-Core Design by Gem5 (Part 2) (01:00/36:54)
Computer Architecture use industry standard simulator to realize their design and assess the performance.
We discuss the gem5 simulator is used for multi-core computer architecture storage and interconnects.
https://www.youtube.com/watch?v=hMj-GB8BTd4&t=31s

## Slide 3: 1.1 What is Gem5?

## Slide 4: 1.1 What is Gem5?
What is Gem5 (01:58/36:54)
The was a popular simulator called M5 by University of Michigan in 2006.
Around the same time, another simulator called GEMS by University of Wisconsin Madison, Madison existed. GEMS maybe even more popular than M5.
Both simulators have some flaws, and therefore, the developers thought that they can combine them together called gem5.
The gem5 combines the goodness of both M5 and GEMS.
https://www.youtube.com/watch?v=hMj-GB8BTd4&t=31s

## Slide 5: 1.1 What is Gem5?
What is Gem5 (02:30/36:54)
gem5 uses the CPU models, ISA (Instruction Set Architecture), IO Devices, and other infrastructure from M5 simulator and the Ruby memory modules including cache coherence protocols and interconnect models from GEMS simulator.
Gem5 became one of the most popular computer simulator.
The popularity of gem5 can be got from the fact that it has around 2900+ citations in 2011. https://www.gem5.org/about/
https://www.youtube.com/watch?v=hMj-GB8BTd4&t=31s

## Slide 6: 1.1 What is Gem5?
What is Gem5 (02:27/36:54)
Gem5 is a modular platform for computer system architecture, including system level architecture and processor microarchitecture.
This means that gem5 can model and simulate everything in computer architecture.
Right from system calls, operating system kernel, processors, memory interconnection, and everything else that we can think of in a computer system.
https://www.youtube.com/watch?v=hMj-GB8BTd4&t=31s

## Slide 7: 1.2 Key Feature

## Slide 8: 1.2 Key Feature
Key Feature (03:40/36:54)
Gem5 runs in two execution modes:
1. System call emulation where only the processor and memory is emulated
2. Full system mode which is equivalent to run a virtual machine on a system.
Gem5 has these binaries for the simulation, gem5.debug, gem5.opt, gem5.prof, gem5.perf, and gem5.fast.
Gem5 also support different ISA (Instruction Set Architecture), like ALPHA (No longer support), ARM, MIPS, POWER, RISCV, SPARC, X85, and NULL.
X86 is one os the popular ISA (Instruction Set Architecture) used in personal computing systems, and
ARM is another popular ISA used in mobile computing systems.
https://www.youtube.com/watch?v=hMj-GB8BTd4&t=31s

## Slide 9: 1.2 Key Feature
Key Feature (04:00/36:54)
Gem5 also support different CPU Models. Like Atomic Simple CPU, Timing Simple CPU, In Order, and O3 (Out of Order) CPU.
Gem5 uses two memory models: classic taken from the 5 Simulator and Ruby taken from the GEMs simulator.
It also supports two different interconnection networks: Simple and Garnet.
https://www.youtube.com/watch?v=hMj-GB8BTd4&t=31s

## Slide 10: 1.2 Key Feature
Key Feature (4:40/36:54)
We discuss system call emulation mode in gem5.opt binary with ALPHA (ARM) ISA (Instruction Set Architecture).
We will use Atomic Simple for CPU, Ruby memory model, and Garnet Interconnect network.
https://www.youtube.com/watch?v=hMj-GB8BTd4&t=31s

## Slide 11: 1.3 Build and Run

## Slide 12: 1.3 Build and Run
Build and Run (5:25/36:54)
Gem5 can be built and run on different operating system platform like Linux, BSD, MacOS, and Solaris on 64 bits machines.
Gem5 has dependencies on gcc, g++, python, scons, SWIG, M4, and Z library.
https://www.youtube.com/watch?v=hMj-GB8BTd4&t=31s

## Slide 13: 1.3 Build and Run
Build and Run (6:56/36:54)
Install dependencies
Get gem5
Build gem5 simulator.
Note:
ALPHA is no longer used in gem5.
We use ARM, RISCV, and X86 instead.
https://www.youtube.com/watch?v=hMj-GB8BTd4&t=31s

## Slide 14: 1.3 Build and Run
Build and Run (7:56/36:54)
> lscpu
>> shows number of CPU.
https://www.youtube.com/watch?v=hMj-GB8BTd4&t=31s

## Slide 15: 1.3 Build and Run
Build and Run (8:56/36:54)
> scons build/ARM/gem5.opt -j 7
Note:
You specify one more than your system have.
For example,
If you have 8 CPUs, you specify “-j 9”
If you have 6 CPUs, then you specify “-j 7”.
https://www.youtube.com/watch?v=hMj-GB8BTd4&t=31s

## Slide 16: 1.3 Build and Run
Build and Run (9:43/36:54)
> ./build/ARM/gem5.opt --help
>> You can different help options from gem5.
https://www.youtube.com/watch?v=hMj-GB8BTd4&t=31s

## Slide 17: 1.3 Build and Run
Build and Run (9:52/36:54)
We can run gem5
> ./build/ARM/gem5.opt configs/example/se.py
> ./build/ARM/gem5.opt configs/example/se.py --help
https://www.youtube.com/watch?v=hMj-GB8BTd4&t=31s

## Slide 18: 1.3 Build and Run
Build and Run (10:52/36:54)
> ./build/ARM/gem5.opt configs/example/se.py --help
> ./build/ARM/gem5.opt configs/example/se.py -c tests/test-progs/hello/bin/arm/linux/hello
https://www.youtube.com/watch?v=hMj-GB8BTd4&t=31s

## Slide 19: 1.3 Build and Run
Build and Run (11:30/36:54)
> ./build/ARM/gem5.opt configs/example/se.py -c tests/test-progs/hello/bin/arm/linux/hello
You can see “Hello world!” message.
After this message, the simulator has nothing to do and just “Exiting @...”
https://www.youtube.com/watch?v=hMj-GB8BTd4&t=31s

## Slide 20: 1.3 Build and Run
Build and Run (12:30/36:54)
We can also try the full system mode (fs.py)
> ./build/ARM/gem5.opt configs/example/fs.py
We do not discuss the full system mode in this discussion.
https://www.youtube.com/watch?v=hMj-GB8BTd4&t=31s

## Slide 21: 1.4 Simulation Flow

## Slide 22: 1.4 Simulation Flow
Simulation Flow (12:48/36:54)
We have python script se.py.
We create the simulation objects and parameters.
We have simulation object described in Python.
Python interpreter compiled into gem5.
Gem5 combines C++ object and perform simulation.
https://www.youtube.com/watch?v=hMj-GB8BTd4&t=31s

## Slide 23: 1.4 Simulation Flow
Simulation Flow (13:21/36:54)
Function call sequences.
https://www.youtube.com/watch?v=hMj-GB8BTd4&t=31s
main.cc
init.cc
main.py se.py -c …
C++ constructors and start simulation

## Slide 24: 1.4 Simulation Flow
Simulation Flow (14:12/36:54)
ARM, RISCV, ALPHA, and etc. are all SimObject.
https://www.youtube.com/watch?v=hMj-GB8BTd4&t=31s
SimObject

## Slide 25: 1.5 Configuration and Output

## Slide 26: 1.5 Configuration and Output
Configuration and Output (14:20/36:54)
After complete simulation, we look at the results in directory m5out.
config.ini: contains all SimObjects created for the simulation. There different objects and parameters foe objects in this file. We can check which parameters we want.
config.json: Same as config.ini but in json format.
https://www.youtube.com/watch?v=hMj-GB8BTd4&t=31s

## Slide 27: 1.5 Configuration and Output
Configuration and Output (16:23/36:54)
stats.txt: Contains all the simulation results.
https://www.youtube.com/watch?v=hMj-GB8BTd4&t=31s

## Slide 28: 1.6 Directory Tour

## Slide 29: 1.6 Directory Tour
Directory Tour (16:49/36:54)
https://www.youtube.com/watch?v=hMj-GB8BTd4&t=31s
Python in front end and backend in c++
Backend in C++ Simulator Objects
Benchmark tests “hello” or others.

## Slide 30: 1.7 Get Binary Test Program for ARM

## Slide 31: 1.7 Get Binary Test Program for ARM
Get Binary Test Programs for ARM (01:48/36:54)
> mkdir -p cpu_tests/benchmarks/bin/arm
> cd cpu_tests/benchmarks/bin/arm
1. > wget dist.gem5.org/dist/v22-0/test-progs/cpu-tests/bin/arm/Bubblesort
2. > wget dist.gem5.org/dist/v22-0/test-progs/cpu-tests/bin/arm/FloatMM
3. > ls
https://www.gem5.org/documentation/learning_gem5/part1/extending_configs
1
2
3

## Slide 32: End