## Slide 1: 2 Cache Memory
Peter H. Chen

## Slide 2: 2 Cache Memory
Cache Memory (00:30/50:44)
What is Cache Memory?
How the Cache memory map to main memory?
https://nptel.ac.in/courses/106103183

## Slide 3: 2.1 CPU vs. Memory Performance Gap

## Slide 4: 2.1 CPU vs. Memory Performance Gap
CPU vs. Memory Performance Gap (01:30/50:44)
https://nptel.ac.in/courses/106103183
Performance of CPU vs DRAM
CPU speed grow much faster than DRAM memory
CPU improve decoding of operation, performing an ALU operation, this lead to an imbalance in the speed of operation.

## Slide 5: 2.2 CPU Pipeline

## Slide 6: 2.2 CPU Pipeline
CPU Pipeline (2:33/50:44)
https://nptel.ac.in/courses/106103183
To solve the imbalance problem between CPU and memory, the memory hierarchy has been proposed.
This is the instruction pipeline.

## Slide 7: 2.2 CPU Pipeline
CPU Pipeline (2:33/50:44)
https://nptel.ac.in/courses/106103183
You can see there are two stages, one is instruction fetch stage and the other one is MEM stage.
Every stage we will talk exactly one clock cycle.
The design challenge is in the instruction fetch stage and MEM stage go along with normal pipeline speed.
Instruction Fetch stage
MEM stage
Decode Stage
Execute Stage
Write Back Stage
RF (Register File)
Instruction Cache
Data Cache

## Slide 8: 2.3 Memory

## Slide 9: 2.3 Memory
Memory (4:30/50:44)
https://nptel.ac.in/courses/106103183
To keep large memory, we implement computer memory as a hierarchy.
Multiple memory with different speeds.
We keep the smaller and faster memories close to CPU and keep the slower and large memory below fast memory.

## Slide 10: 2.4 Memory Hierarchy

## Slide 11: 2.4 Memory Hierarchy
Memory Hierarchy (5:30/50:44)
https://nptel.ac.in/courses/106103183
We can see there are two types of L1 cache:
1. L1 Instruction Cache, during the fetch stage and
2. L1 Data Cache, during the MEM stage.
We have these two dedicated caches to avoid structural hazard. One cache exclusively for instruction, one exclusively for data to separate read and write.
Core:
CPU, Register File, L1 Cache

## Slide 12: 2.4 Memory Hierarchy
Memory Hierarchy (6:30/50:44)
https://nptel.ac.in/courses/106103183
We have very high speed RF (Register File), then we have a little bit slower L1 Cache, and slower L2 Cache, and then very slow DRAM memory.

## Slide 13: 2.5 Cache Memory

## Slide 14: 2.5 Cache Memory
Cache Memory (9:18/50:44)
https://nptel.ac.in/courses/106103183
Principle of Locality:
1. Temporal locality: The probability to access the same location of in near future in time T is very high, typically programs has loops or control structures which help us the go back the same of code again.
2. Spatial locality: If the location of L is accessed in time T, then the probability of location L plus delta L to be access in time T plus delta T is also very high. That means, if you access a location now its nearby locations will be accessed in the immediate future.
If CPU request a word from main memory, it can be get previous word from cache memory.

## Slide 15: 2.6 Access Pattern

## Slide 16: 2.6 Access Pattern
Access Pattern (12:19/50:44)
https://nptel.ac.in/courses/106103183
We can see same addresses are access many times.

## Slide 17: 2.7 Cache Fundamentals

## Slide 18: 2.7 Cache Fundamentals
Cache Fundamentals (15:19/50:44)
https://nptel.ac.in/courses/106103183

## Slide 19: 2.8 CPU - Cache Interaction

## Slide 20: 2.8 CPU - Cache Interaction
CPU – Cache Interaction (16:53/50:44)
https://nptel.ac.in/courses/106103183
Register file: 1 Word = 4 bytes
Cache memory: two 4-words blocks
main memory: many 4-words blocks

## Slide 21: 2.9 Cache Organization

## Slide 22: 2.9 Cache Organization
Cache Organization (19:07/50:44)
https://nptel.ac.in/courses/106103183
Cache memory:
1. Cache has array of S sets. Set 0, set 1, …
2. Each set has multiple lines (E)
3. Each line has B (= 2^b bytes) blocks.
When have 64 kB caches.
1. Each cache has S sets.
2. Each set divided into E lines.
3. Each line has B blocks.

## Slide 23: 2.10 Addressing Cache

## Slide 24: 2.10 Addressing Cache
Addressing Cache (20:48/50:44)
https://nptel.ac.in/courses/106103183

## Slide 25: 2.10 Addressing Cache
Addressing Cache (23:50/50:44)
https://nptel.ac.in/courses/106103183

## Slide 26: 2.11 Four Cache Memory Design Choices

## Slide 27: 2.11 Four Cache Memory Design Choices
Four Cache Memory Design Choices (24:41/50:44)
https://nptel.ac.in/courses/106103183

## Slide 28: 2.12 Block Placement

## Slide 29: 2.12 Block Placement
Block Placement (26:57/50:44)
https://nptel.ac.in/courses/106103183
Each block of main memory is mapped to cache memory.
For example,
1. block 12 in main memory. 12 % 8 = 4. It is block 4 in the cache memory.
2. Block 16 in main memory. 16 % 8 = 0. It is block 0 in cache memory.
3. Block 24 in main memory. 24 % 8 = 0. It is block 0 in cache memory.
Multiple block in main memory may be mapped to the same cache memory.

## Slide 30: 2.12 Block Placement
Block Placement (26:57/50:44)
https://nptel.ac.in/courses/106103183
If we have two set in cache memory.
Now the module function is 4.
1. Block 12 in main memory. 12 % 4 = 0 in cache memory.
2. Block 21 in main memory. 21 % 4 = 1 in cache memory.
We can have 4-way associate (4 blocks).

## Slide 31: 2.12 Block Placement
Block Placement (26:57/50:44)
https://nptel.ac.in/courses/106103183
All cache memory into one block.
We called fully associate.
Any block in main memory can be place anywhere.

## Slide 32: 2.12 Block Placement
Block Placement (32:36/50:44)
https://nptel.ac.in/courses/106103183

## Slide 33: 2.13 Direct-Mapped Cache

## Slide 34: 2.13 Direct-Mapped Cache
Direct-Mapped Cache (32:36/50:44)
https://nptel.ac.in/courses/106103183

## Slide 35: 2.14 Accessing Direct-Mapped Cache

## Slide 36: 2.14 Accessing Direct-Mapped Cache
Accessing Direct-Mapped Cache (33:18/50:44)
https://nptel.ac.in/courses/106103183

## Slide 37: 2.14 Accessing Direct-Mapped Cache
Accessing Direct-Mapped Cache (34:17/50:44)
https://nptel.ac.in/courses/106103183

## Slide 38: 2.14 Accessing Direct-Mapped Cache
Accessing Direct-Mapped Cache (35:35/50:44)
https://nptel.ac.in/courses/106103183

## Slide 39: 2.15 Block Identification

## Slide 40: 2.15 Block Identification
Block Identification (36:53/50:44)
https://nptel.ac.in/courses/106103183
If “=“, then hit.

## Slide 41: 2.16 Direct Mapped Cache

## Slide 42: 2.16 Direct Mapped Cache
Direct Mapped Cache (37:29/50:44)
https://nptel.ac.in/courses/106103183

## Slide 43: 2.17 Set Associative Cache

## Slide 44: 2.17 Set Associative Cache
Set Associative Cache (39:04/50:44)
https://nptel.ac.in/courses/106103183

## Slide 45: 2.18 Accessing Set Associative Cache

## Slide 46: 2.18 Accessing Set Associative Cache
Accessing Set Associative Cache (39:08/50:44)
https://nptel.ac.in/courses/106103183

## Slide 47: 2.18 Accessing Set Associative Cache
Accessing Set Associative Cache (39:18/50:44)
https://nptel.ac.in/courses/106103183
matched

## Slide 48: 2.18 Accessing Set Associative Cache
Accessing Set Associative Cache (40:35/50:44)
https://nptel.ac.in/courses/106103183

## Slide 49: 2.18 Accessing Set Associative Cache
Accessing Set Associative Cache (40:35/50:44)
https://nptel.ac.in/courses/106103183

## Slide 50: 2.18 Accessing Set Associative Cache
Accessing Set Associative Cache (43:39/50:44)
https://nptel.ac.in/courses/106103183
No index in fully associative

## Slide 51: 2.19 Cache Indexing

## Slide 52: 2.19 Cache Indexing
Cache Indexing (43:50/50:44)
https://nptel.ac.in/courses/106103183
0 t0 31: total have 32 sets

## Slide 53: 2.19 Cache Indexing
Cache Indexing (45:19/50:44)
https://nptel.ac.in/courses/106103183
Use higher order bit indexing to avoid same cache mapping.
Lower order bit will map to different cache mapping.
Tag
Index
Block offset

## Slide 54: End