## Slide 1: 3 Basic Cache Optimization (Part 4)
Peter H. Chen

## Slide 2: 3 Basic Cache Optimization
Basic Cache Optimization (30:04/43:50)
30:04 Now, we have something called inclusive and exclusive caches.
So, cache memory itself by virtue of the organization, we are dividing them into inclusive and exclusive caches.
So, inclusive cache means multiple hierarchy is actually a subset.
So, when you have a cache architecture in which your L1 cache is a subset of L2 then we call it as an inclusive cache; if we have L1 and L2 both are mutually exclusive that means, there is nothing in common in L1 and L2 we call it is an exclusive cache.
So, as the summary I am going to repeat once again inclusive cache means a subset of L2 is taken to L1.
So, whatever is there in L1; it will surely be there in L2 also.
Exclusive cache means, whatever is there in L1; it will be never be there in L2, this means the effective cache memory size if it is an exclusive cache will be more, because
https://nptel.ac.in/courses/106103183
Exclusive: L1 and L2 are independent
Inclusive L1 and L2 are dependent

## Slide 3: 3 Basic Cache Optimization
Basic Cache Optimization (31:08/43:50)
the size of L1 plus size of L2 is effective cache size whereas, in this case of an inclusive cache the effective cache size is equal to the size of L2 because, L1 size is actually taken away from L2.
31:22 This is yet another way of looking at an inclusive cache size hierarchy, whenever we get a core request the request is going into L1, and then whenever it is missed you can go into the L2 that is called the last level cache.
And whenever a block is to be evicted then you are evicting from L1 into L2.
31:48 L1 is actually a subset of last level cache, but when in this case whenever there is a request.
The request is directly going to come from memory, rather than filling up in last level cache is directly going in filling in first level cache, eviction happened from there into that.
https://nptel.ac.in/courses/106103183

## Slide 4: 3 Basic Cache Optimization
Basic Cache Optimization (32:06/43:50)
So, L1 is not in last level cache that is called an exclusive cache size hierarchy.
Next optimization is yet another way to reduce miss penalty is to give priority to read misses over writes.
32:20 Consider the scenario if a read miss has to evict a dirty memory block, the normal sequence is write the dirty block to memory and then read the miss block.
32:56 Consider the case these are all RISC instruction, store word R3 512 of R0 that means content of register R3 is going to be stored into memory say location 512.
Then I have to load a value from memory location 1024 into R1 and then yet another is and loading 6one more value from again this memory location.
32:59 So, now the peculiarity is when you perform the split up of the blocks; the first one has to perform a write on location 512 or essentially it is a block 512.
https://nptel.ac.in/courses/106103183
Store a word from register3 memory
Load a word from memory to register

## Slide 5: 3 Basic Cache Optimization
Basic Cache Optimization (33:11/43:50)
33:11 The second instruction will perform a read on location 1024 and the third one is again read on location 512.
33:22 In this case, it is basically a conflict that is going to work here.
So, you are going to have a write operation, we have going to write something into block 512 after that we are going to read a location.
Now, once this write going to happen in memory, in the meantime I wanted to have a read assume that these read is a miss.
Once the read is a miss you are supposed to bring the block, but when the write is happening into the same block in which the read is going to be performed, then it is always better to prioritize this read over write.
34:09 If a read a miss has to evict a dirty memory block, the normal sequence is write the dirty block first, we are going to complete the write and then we are going to read.
https://nptel.ac.in/courses/106103183

## Slide 6: 3 Basic Cache Optimization
Basic Cache Optimization (34:14/43:50)
34:18 The optimization can be first you copy the dirty block to a buffer, then do you read from the memory and then write the block thereby your write operation will be slightly delayed and your read operation is been prioritize over the writes such that you can improve the performance.
34:35 In write through caches, write buffers hold the updated value of the block and the when you encounter with the read miss, you have to read from this write buffer as well.
34:49 What do you mean by write through cache, we have seen in our last lecture; caches are divided into two based upon where write’s updates are happening.
If it is a write through cache then any writing on cache memory it is reflected in main memory as well at the same time such that cache memory and main memory are coherent.
https://nptel.ac.in/courses/106103183

## Slide 7: 3 Basic Cache Optimization
Basic Cache Optimization (35:00/43:50)
35:06 When you are using the write back cache, all the writes happen on the first level cache only, only when there is an eviction from the first level cache then only the updated writes goes to the next level of memory.
So, when you have a write through cache this every write that happens on cache memory has to happen along in main memory also, processor need not wait until the main memory write is over.
36:04 So, cache whatever value that is written in cache, a copy is kept in a buffer known as a write buffer which will parallelly write it into main memory.
So, processor will continue its task by putting the appropriate data to be written in the write buffer, the queue is serviced, the contents should be updated in the main memory.
https://nptel.ac.in/courses/106103183

## Slide 8: 3 Basic Cache Optimization
Basic Cache Optimization (35:51/43:50)
35:51 So, when you encounter a read miss then rather than directly going to main memory sometimes the value might have just the returned and the block is evicted, it may be present in the write buffer.
36:04 So, searching in write buffer sometimes will help either wait till write buffer is empty or search in the write buffer before going to the memory.
Now, we will see the sixth optimization for the day.
https://nptel.ac.in/courses/106103183

## Slide 9: 3 Basic Cache Optimization
Basic Cache Optimization (36:30/43:50)
Avoid address translation for indexing.
We know that CPU is giving you virtual address and this virtual address has to be converted into physical address before accessing the data from the cache.
So, what do you mean by physical address?
Physical address means it is the address of the location, when it is present inside main memory; but when CPU is giving a virtual address you have to convert it into physical address and that translation is done with the help of main memory, memory management unit and translate lookaside buffer.
36: 48 So, you have page tables that converts your virtual pages into physical frames and then using offset, these are the concepts typically we learn in operating systems course.
So, virtual address to physical address has to be done before cache a lookup.
Now, we know that once you access cache there are two operation that is involved.
https://nptel.ac.in/courses/106103183

## Slide 10: 3 Basic Cache Optimization
Basic Cache Optimization (37:09/43:50)
First you have to index into the corresponding set, one should index into the set the tag value which is stored in the set is extracted and it is compared with the incoming tag in the address.
37:20 So, indexing happens first followed by tag comparison.
So, if the indexing can be done only if you get the physical address then before going to indexing first step should have been converting from virtual address to physical address that is when CPU gives an address the virtual address, first stage is using a memory management unit or a translation local side buffer convert the virtual address into the physical address.
And once you get the physical address then divide into tag index and offset, you are using the index bit go and refer in to the location and then you perform tag comparison.
https://nptel.ac.in/courses/106103183

## Slide 11: 3 Basic Cache Optimization
Basic Cache Optimization (38:04/43:50)
Since there is a translation time that is involved, accessing cache is going be very slow and if it is an L1 cache then your instruction pipeline also has to be stalled.
The idea the optimization idea is since you are indexing is happening not with the most significant bits.
Let us say the virtual address portion or the physical address portion in the index bit is remaining unaffected then index using virtual address; start indexing with the virtual address in the meantime do the address translation and get the physical address and the tag.
So, your tag portion is inside the physical address whereas, in indexing will be part of the virtual address bits.
So, the role of TLB, TLB access is actually in the critical path.
https://nptel.ac.in/courses/106103183

## Slide 12: 3 Basic Cache Optimization
Basic Cache Optimization (38:50/43:50)
38:50 So, the idea of this optimization is indexing by virtual address and tagging by physical address this is known as virtually index physically tagged cache.
https://nptel.ac.in/courses/106103183

## Slide 13: 3 Basic Cache Optimization
Basic Cache Optimization (39:40/43:50)
39:40 So, we would like to give an illustrative exercise here.
Consider the case that CPU is going to give us a virtual address that consist of 12 bits of offset and 20 bits of page number.
So, what happens is this is going to be converted into say 10 bits of physical frame, so and 12 bits of offset.
So, this translation from 20 bit page number into 10 bit frame number, this is taken care of by your page table or TLB.
So, it is this is your physical address and only if you get the physical address then only you can divide into tag, index and offset;
this optimization principal is saying that if your index and offset is within this 12 bits, if your index and offset values are within this 12 bits.
https://nptel.ac.in/courses/106103183
Tag | Index | offset

## Slide 14: End