## Slide 1: 4 Cache Memory Optimization (Part 2)
Peter H. Chen

## Slide 2: 4.3 Problem 3 (Continue)

## Slide 3: 4.3 Problem 3
Cache Memory Optimization (Part 2) (00:32/40:09)
10:11 So, miss rate is going to be 10 percent 0.1 into miss penalty is 300.
10:17 So, you will get a value 35.
10:20 So, average memory access time for the first case is 35, 35 nanosecond.
10:25 Why we compute average memory access time?
10:28 Because second portion of the question is if doubling the cache memory, if doubling
10:33 the cache memory block size will reduce is going to reduce your miss rate to 3 percent
10:39 does it reduce average memory access time.
10:41 So, for first case average memory access time is 35.
10:45 Let us see what is the next case; so, we have in case 1 our average memory access time is
10:51 35 nanosecond.
10:54 Now in case 2 we are going to double the block size.
10:58 So, the number of words so, my block size is now 128 byte divided by 4 byte is one word
https://nptel.ac.in/courses/106103183

## Slide 4: 4.3 Problem 3
Cache Memory Optimization (Part 2) (00:32/40:09)
11:08 so, you have now 32 words.
11:10 Now, when you take the miss penalty out of 32 word the first word is going to take 150
11:17 nanosecond.
11:18 Plus, you have 31 more words.
11:20 Each word is going to take 10 more nanosecond each.
11:23 So, it is 150 plus 310 that is going to be 460.
11:30 So, 460 nanosecond is the miss penalty of the optimized cache.
11:35 Now, let us try to find out what is the average memory access time with this one.
https://nptel.ac.in/courses/106103183
Double the block size = 128B

## Slide 5: 4.3 Problem 3
Cache Memory Optimization (Part 2) (00:32/40:09)
11:42 So, average memory access time is to be defined as hit time.
11:48 So, the hit time value is same 5 plus, miss rate is come down to 0.03 into(x) 460.
12:00 And this is going to give you 18.8 nanosecond.
12:03 So, with the optimization so we can see that with the optimization, the average memory
12:13 access time is 18.8 nanosecond.
https://nptel.ac.in/courses/106103183

## Slide 6: 4.4 Problem 4
Cache Memory Optimization (Part 2) (00:32/s40:09)
12:15 Whereas, the first case it was 35 nanosecond.
12:20 So, the question of if doubling the cache block size reduce miss rate to 3 percent,
12:24 does it reduce average memory access time?
12:27 The answer is yes.
https://nptel.ac.in/courses/106103183

## Slide 7: 4.4 Problem 4

## Slide 8: 4.4 Problem 4
Cache Memory Optimization (Part 2) (00:32/40:09)
12:28 Now, we move want to the fourth problem.
12:31 For a cache that has a miss rate of 3 percent and the miss penalty of 500 cycles.
12:38 In a program it was found that 50 percent of instructions are memory accesses that basically
12:43 load and store.
12:45 Find misses per 1000 instruction or it is also known as MPKI.
12:50 MPKI is a common measurement or a metric that is used in cache memory domain to express
12:57 how many hits or miss are there in a cache.
13:00 So, it is based upon the number of programs number of instruction that are executed misses
13:05 per kilo instruction.
https://nptel.ac.in/courses/106103183

## Slide 9: 4.4 Problem 4
Cache Memory Optimization (Part 2) (00:32/40:09)
13:06 So, for every 1000 instruction that I fetch how many misses that is occurring.
13:12 So, we will try to solve this problem.
13:15 Miss rate is typically defined as number of misses encountered divided by number of memory
13:21 access need.
13:22 It can also be defined as misses per instruction divided by memory access per instruction because;
13:28 if the instruction side get cancelled it is same as misses per memory access.
13:33 So, the conventional equation of miss rate; which is defined as number of misses divided
13:38 by number of memory access.
13:40 We can also be written as misses per instruction divided by memory access per instruction.
13:47 This we could represent it as MR.
13:50 MR stands for Miss Rate is defined as MPI misses per instruction divided by MAPI memory
13:57 access per instruction.
13:58 Or if you wanted to get what is MPI, it is miss rate into(x) memory access per instruction.
https://nptel.ac.in/courses/106103183

## Slide 10: 4.4 Problem 4
Cache Memory Optimization (Part 2) (00:32/40:09)
13:06 So, for every 1000 instruction that I fetch how many misses that is occurring.
13:12 So, we will try to solve this problem.
13:15 Miss rate is typically defined as number of misses encountered divided by number of memory
13:21 access need.
13:22 It can also be defined as misses per instruction divided by memory access per instruction because;
13:28 if the instruction side get cancelled it is same as misses per memory access.
13:33 So, the conventional equation of miss rate; which is defined as number of misses divided
13:38 by number of memory access.
13:40 We can also be written as misses per instruction divided by memory access per instruction.
13:47 This we could represent it as MR.
13:50 MR stands for Miss Rate is defined as MPI misses per instruction divided by MAPI memory
13:57 access per instruction.
13:58 Or if you wanted to get what is MPI, it is miss rate into(x) memory access per instruction.
https://nptel.ac.in/courses/106103183

## Slide 11: 4.4 Problem 4
Cache Memory Optimization (Part 2) (00:32/40:09)
14:05 So, the miss rate value is been defined as 0.03 that is our miss rate.
14:16 Now memory access per instruction is 1.5 from where did we get this value.
14:23 Let us try to see that.
14:25 It was mentioned that you have 50 percent of instructions are memory access.
14:30 So, for an instruction there is minimum one memory access, because when you go and fetch
14:35 an instruction during the instruction fetch stage.
14:39 That is one time do you access a memory, the first time that you access memory.
14:43 If it is a load store instruction, then during the mem stage also you are going to access
14:48 the memory.
14:49 So, they will be 2 times for every load store instruction, we are going to access memory
14:55 two times.
14:56 But for every other instruction you are going to access memory one time.
14:59 So, on an average we have 50 percent of the instruction which are load store.
https://nptel.ac.in/courses/106103183

## Slide 12: 4.4 Problem 4
Cache Memory Optimization (Part 2) (00:32/40:09)
15:05 Meaning, average access per instruction average memory access per instruction is 1.5.
15:12 So, your misses per instruction is 0.045.
15:19 Now this is actually MPI 0.045.
15:29 Now MPKI misses per kilo instruction is defined as MPI into(x) 1000.
15:42 So, our MPI value is 0.045.
15:46 So, MPKI is equal to 45.
15:51 So, MPKI is a new measurement, miss rate into(x) memory access per instruction that is called
15:58 misses per kilo instruction.
https://nptel.ac.in/courses/106103183

## Slide 13: 4.4 Problem 4
Cache Memory Optimization (Part 2) (00:32/40:09)
16:01 That is what we have obtained.
16:02 Now the next portion is find memory stall cycles per miss.
16:08 The memory stall cycles per miss is defined as miss rate into miss penalty your miss rate
16:16 is equal to 0.03 into(x) miss penalty is equal to 500.
16:21 So, the memory stalls is 15.
16:27 On an average every miss will have 15 cycles of memory stall.
16:36 So, memory stalls is defined memory stall cycles per miss.
16:39 For every miss you are going to have 15 cycles on an average, memory stalls per cycle.
https://nptel.ac.in/courses/106103183

## Slide 14: 4.5 Problem 5

## Slide 15: 4.5 Problem 5
Cache Memory Optimization (Part 2) (00:32/40:09)
16:47 Next we move on to the fifth problem.
16:49 Consider a cache system with a miss rate of an I-cache.
16:53 So, here this we have a separate cache I and D-cache is separate.
16:57 Consider a cache system with a miss rate of I-cache is equal to 2 percent and D-cache
17:01 is equal to 4 percent.
https://nptel.ac.in/courses/106103183

## Slide 16: 4.5 Problem 5
Cache Memory Optimization (Part 2) (00:32/40:09)
17:03 The processor CPI is equal to 2 without memory stalls and miss penalty.
17:06 So, these may be the stalls with hazards alone.
17:09 Without any memory stalls or without any misses with respect to caches you are going to have
17:15 a CPI of 2.
17:16 If you miss the miss penalty is 100 cycles.
17:19 Determine how much faster the processor would run if it is a perfect cache that never missed.
17:25 Assume frequency of load and store is 36 percentage.
17:29 Now in solving this question, you see that for an ideal processor it is mentioned that
17:36 CPI is equal to 2.
17:38 Now for your real processor CPI is base CPI plus memory stall CPI.
17:44 Now the stall CPI how many stalls you are going to incur, you can have stalls in the
17:48 I-cache during the instruction fetch stage.
17:51 You can have stalls in the D-cache during the mem stage.
17:55 So, stall CPI is percentage use of I-cache into(x) stalls of the I-cache, plus percentage
https://nptel.ac.in/courses/106103183
CPI (Cache Performance Index)
Effective CPI = Baseline CPI + CPI of memory accesses
Baseline CPI is 1 (given in the problem statement). So you just need to find the CPI of the memory accesses.
If the memory access is a hit in the cache then we assume that the CPI is the same as the baseline CPI. If it is a miss then it will be the miss latency.
So you have 33% of instructions that are memory accesses. Of those the ones that are misses will take 10 cycles.
So putting all of this together you get:
CPI = miss rate*(.3333)*10 + 1

## Slide 17: 4.5 Problem 5
Cache Memory Optimization (Part 2) (00:32/40:09)
18:01 use of D-cache into(x) the stalls of D-cache.
18:05 Now how will you find out what is a percentage of time you are going to use the I-cache.
18:09 So, I-cache miss rate is 2 percent, D-cache miss rate is 4 percent.
18:15 And miss penalty is going to be 100 cycles.
18:18 It is mentioned that frequency of load store is 36 percent.
18:22 Only when there is a load store then only we are going to access the D-cache.
18:25 So, out of 100 instruction 36 instructions are load store instruction, meaning they will
18:31 have access to the data memory also.
18:36 So, when you have 100 instructions, all these 100 instructions will go to I-cache.
18:40 Out of this 100 instruction 36 of them will go to D-cache.
18:44 So, how many times you go to cache?
18:47 100 times to I-cache 36 time to D-cache, together 136 times you are going to the cache.
18:54 So, what is the percentage you use?
18:56 Out of the 100 and 36 times, 100 times I am going to I-cache.
https://nptel.ac.in/courses/106103183

## Slide 18: 4.5 Problem 5
Cache Memory Optimization (Part 2) (00:32/40:09)
19:01 So, 100 by 136 into(x) what is the stall cycles?
19:07 Miss rate into miss penalty 0.02 into(x) 100.
19:13 This is the stalls from the I-cache.
19:17 And for D-cache how many times you go you go only 36 times out of the 136 times.
19:22 Only 36 times we go to D-cache, and the stalls that is coming over here is like this.
19:30 Remember, we have to multiply the stalls with the weight factor equal to the percentage
19:38 use of the corresponding cache.
19:40 So, this is what you get 1.47 will be the left side and the right side 1.06.
19:50 Altogether making it has 2.53.
19:55 So, the stall cycles is 2.53 and what is the actual CPI now?
https://nptel.ac.in/courses/106103183

## Slide 19: 4.5 Problem 5
Cache Memory Optimization (Part 2) (00:32/40:09)
19:55 So, the stall cycles is 2.53 and what is the actual CPI now?
20:02 The base CPI of 2 plus 2.53 so, total we have 4.53 is the CPI of the real machine.
20:17 So, what is the overall speed up that you are going to get.
https://nptel.ac.in/courses/106103183

## Slide 20: 4.5 Problem 5
Cache Memory Optimization (Part 2) (00:32/40:09)
20:20 Speed up is defined as CPI with the modification.
20:24 So, the speed up that you are going to get is 4.53 divided by the CPI of the ideal machine
20:32 is 2.
20:33 So, it is 2.265 times.
20:38 So, the answer the speed up is 2.265.
https://nptel.ac.in/courses/106103183

## Slide 21: 4.5 Problem 5
Cache Memory Optimization (Part 2) (00:32/40:09)
20:41 So, in order to re-summarize this question; in the question the miss rate of I-cache and
20:56 D-cache is given, what is the percentage of load store instruction is given.
https://nptel.ac.in/courses/106103183

## Slide 22: 4.5 Problem 5
Cache Memory Optimization (Part 2) (00:32/40:09)
21:00 Percentage of load store instruction will really help us to find out how what is the
21:05 fraction of time that we are going to use D-cache.
21:09 If you have 36 percent of instructions which are load store, then in 100 instruction 36
21:16 instructions will be load store means I go to D-cache 36 times.
21:19 So, out of 136 times that I go to cache 100 times to I-cache and 36 times to D-cache,
21:24 I can easily find out the fraction.
21:26 So, that is the reason 100 by 136 is the fraction of time I go to I-cache.
21:31 36 by 136 is the fraction of time that we go to D-cache.
https://nptel.ac.in/courses/106103183

## Slide 23: 4.5 Problem 5
Cache Memory Optimization (Part 2) (00:32/40:09)
21:36 And this is the miss rate into miss penalty component.
21:38 So, upon solving we get stalls of 2.53 our ideal case is 2.
21:45 So, 2 plus 2.53, 4.53 is the stall.
21:49 And if you look at the speed up it is 4.53 that is the CPI of the real machine divided
21:54 by 2 that is CPI of the ideal machine.
21:58 This is the way how we are going to solve this.
https://nptel.ac.in/courses/106103183

## Slide 24: 4.6 Problem 6

## Slide 25: 4.6 Problem 6
Cache Memory Optimization (Part 2) (00:32/40:09)
22:00 Now, will move to problem number 6, in problem number 6 we have given a scenario of a hierarchical
22:07 cache memory with an L1 cache and an L2 cache.
22:09 The address of a program and it is corresponding data is also given.
22:13 And we have to find out through which all set numbers is data will move.
22:18 Consider a 32-bit processor with the 16 KB direct mapped L1 cache, that use a block size
22:23 of 4 words.
22:24 So, let us try to stress on the important kinds.
22:28 It is a 32-bit processor, 16 KB direct mapped L1 cache that use a block size of 4.
22:34 It was an L2 cache of 256 KB which is 4 way associative with a block size of 8 words.
22:42 System use a byte addressable 256 MB DRAM.
22:47 Upon running a program 16 consecutive fix the length instruction, each instruction is
22:52 also one word one word is given of 32 bit.
22:54 So, we have each instruction is 4 byte, starting at main memory address 0x8226620 are executed.
https://nptel.ac.in/courses/106103183

## Slide 26: 4.6 Problem 6
Cache Memory Optimization (Part 2) (00:32/40:09)
23:01 These instructions operate on an array a of 8 words.
23:07 With starting address 42AF578.
23:12 Assuming caches are initially empty indicate the non-empty sets on L1 cache and L2 cache
23:17 after the execution.
https://nptel.ac.in/courses/106103183

## Slide 27: 4.6 Problem 6
Cache Memory Optimization (Part 2) (00:32/40:09)
23:18 Let us try to summarize what is given in the question.
23:22 You have the processor whose word length is 4 bytes 32 bit.
23:27 Now you have 2 levels of cache; L1 cache and L2 cache.
23:30 Now, L1 cache as a capacity of 4 words, L2 cache as a capacity of 8 words; L1 cache is
23:36 directly mapped, it is 16 KB. L2 cache is 256 KB it is 4 way associative.
23:41 The main memory system has 256 MB RAM so; that means, physical address is 28 bit, 256
23:49 MB is 2 power 28.
23:51 Now upon running program, you are telling that there are 16 instructions that are fetched.
23:56 The from where it is fetched than address is given.
23:58 So, if you split the address into tag index and offset you know where this is getting
https://nptel.ac.in/courses/106103183

## Slide 28: 4.6 Problem 6
Cache Memory Optimization (Part 2) (00:32/40:09)
24:03 mapped.
24:04 Similarly, upon execution of this instruction they are going to access an array whose address
24:08 is also given.
24:09 So, 8 words of the array is also accessed.
24:12 16 words from I-cache or from the instruction, and 8 words from the data is accessed they
24:18 initially.
24:19 Since the cache is empty first they are brought to L2 then they are brought to L1.
24:23 After the program is done we have to find out which are the places or set numbers in
24:31 these respective caches.
https://nptel.ac.in/courses/106103183

## Slide 29: 4.6 Problem 6
Cache Memory Optimization (Part 2) (00:32/40:09)
24:32 This is what is being given it is a 32-bit processor.
24:35 One word is 4 bytes, 256 MB DRAM so; that means, it is 28 bit address.
24:39 So, these are the data that is given.
24:41 Now, L1 cache is directly mapped in 16 KB directly mapped with block size of 4 words.
24:49 So, when you have block size of 4 words, 4 words into(x) each of the word is 4 byte that
24:55 gives you my block sizes 16 bytes.
24:58 Now let us find out what is the number of sets in the L1 cache.
25:05 Cache size is 16 KB.
25:06 So, it is 2 power 14 divided by block size it is 16 bytes that is 2 power 4 into associativity
25:16 is one that is direct mapped.
25:18 So, it gets 2 power 10.
25:20 So, we got to that the number of sets is 2 power 10.
https://nptel.ac.in/courses/106103183
28 bits address = 2^8 x 2^10 = 256 MB
4 words = 4 x 4 bytes = 16 bytes

## Slide 30: 4.6 Problem 6
Cache Memory Optimization (Part 2) (00:32/40:09)
25:24 So, when you split the address.
25:27 You have 10 bits in the index.
25:29 Your block size is 16 bytes.
25:32 So, you have 4 bits for the offset.
25:36 Now within this 4 bit the 2 bit will tell what is the word.
25:39 So, I can accommodate only 4 words, these first 2 bits will tell which is the word and
25:44 the last 2 bit is actually byte within this word.
25:47 So, 10 plus 4, 14 I have total of 28 bits.
25:52 So, I have a tag of 14.
25:54 This is how you are going to solve.
25:57 So, when you have an address, from the address these 10 bits has to be extracted.
https://nptel.ac.in/courses/106103183

## Slide 31: 4.6 Problem 6
Cache Memory Optimization (Part 2) (00:32/40:09)
26:05 Now if you go to the L2 cache it is 256 KB. 4 way associative and block size is 8 words.
26:13 So, when you are block size is 8 words, 8 words each of the word is going to be 4 bytes.
26:19 So, 32 byte is going to be your block size.
26:22 Let us find out the number of sets in the L2 cache, 256 k that makes it up to 2 power
26:33 18 divided by; block size is 2 power 5, the associativity is 2 power 2 it is 4 way associative.
26:44 So, equation is cache size divided by block size into(x) associativity.
26:47 So, it is 2 power 18 divided by 2 power 7.
26:54 So, that will give you 2 power 11.
26:58 So, the split up is you have 11-bit index and 5 bit offset, and you have a 12 bit tag
27:07 is; this 5 bits you are going to divide into 3 and 2.
https://nptel.ac.in/courses/106103183

## Slide 32: 4.6 Problem 6
Cache Memory Optimization (Part 2) (00:32/40:09)
27:11 The first 3 bits of this 5 bit will tell you; which is the word that is out there are totally
27:16 8 words.
27:17 So, 3 bits are required for word.
27:19 And the remaining 2 bit is byte within this word.
27:21 So, with this we have found out what are the total number of set numbers.
https://nptel.ac.in/courses/106103183

## Slide 33: 4.6 Problem 6
Cache Memory Optimization (Part 2) (00:32/40:09)
27:26 And once you have the address with you, it is these 10 bits what is mentioned in this
27:31 L1 cache, you find out these 10 bits that will tell you to which set number it is mapped,
27:36 look at these 11 bits it will tell you to which set number it is mapped in the L2 cache.
https://nptel.ac.in/courses/106103183

## Slide 34: 4.6 Problem 6
Cache Memory Optimization (Part 2) (00:32/40:09)
27:44 Now, instruction 0x8226620 16 consecutive fixed length instructions, each is one word
27:50 and this is what is your data.
27:52 So, once you have the split up we can further find it out.
https://nptel.ac.in/courses/106103183

## Slide 35: 4.6 Problem 6
Cache Memory Optimization (Part 2) (00:32/40:09)
27:56 So, L1 cache is 16 KB this directly mapped we have told; that is, so the split up of
https://nptel.ac.in/courses/106103183

## Slide 36: 4.6 Problem 6
Cache Memory Optimization (Part 2) (00:32/40:09)
28:01 the L1 cache is you have 14 plus 10 plus 4.
28:07 This is going to be the split up of L1 cache.
28:09 Let us find out how are you going to get this split up.
28:14 Now you have 8226620.
28:16 So, when you write this 8226620, out of it this 10 bit has to be extracted.
28:24 So, I am going to write this portion only 6620.
28:30 6 is 0110, next 6 is 0110.
28:35 2 is 0010 and the last 0 is 0000.
28:40 So, in this there are actually 16 bits out of which this 14 bits we have to extract.
28:46 So, these 14 bits is this.
28:51 So, when I take a block, we can see that from the offset it is on the beginning of the block
https://nptel.ac.in/courses/106103183

## Slide 37: 4.6 Problem 6
Cache Memory Optimization (Part 2) (00:32/40:09)
29:01 itself.
29:02 So, 1001100010 is the 10-bit value which will tell to which the set number this is going
29:11 to map 1001100010.
29:16 This value with 610 if you convert this binary value into decimal the value is 610.
29:22 So, 610 set will accommodate 4 words.
29:28 Then 611 will accommodate another 4 words, 612 will accommodate the next 4 words, and
29:37 613 will accommodate the next 4 words.
https://nptel.ac.in/courses/106103183

## Slide 38: 4.6 Problem 6
Cache Memory Optimization (Part 2) (00:32/40:09)
29:40 So, together I have now 16 words that are getting accessed.
29:45 So, 612 to 613, these 4 set numbers of your L1 cache will be occupied upon successfully
29:54 bringing 16 instruction words from the location 0x8226620.
29:59 Now, if you look at the data portion.
https://nptel.ac.in/courses/106103183

## Slide 39: End