## Slide 1: 4 Adv Cache Optimization Technique II (Part 1)
Peter H. Chen

## Slide 2: 4 Adv Cache Optimization Technique II (Part 1)
Advanced Cache Optimization Technique II (Part 1) (00:32/17:43)
10:15 So, we may not be able to get exactly the
10:17 value of x immediately, multiple times you have to do, but surely this blocking technique
10:23 is going to reduce the memory access time by effectively reducing the miss rate.
https://nptel.ac.in/courses/106103183

## Slide 3: 4 Adv Cache Optimization Technique II (Part 1)
Advanced Cache Optimization Technique II (Part 1) (00:32/17:43)
10:30 Next optimization is known as hardware prefetching; the idea of prefetching means a block is brought to the cache memory before it is requested. When a block is requested we call it as a
10:44 demanded block then the appropriate block is being brought into cache memory up on demand.
10:50 Can we have some mechanisms by which we could predict what is going to be the future demands
10:57 and then bring those blocks apriory such that whenever they are really needed; they are
https://nptel.ac.in/courses/106103183

## Slide 4: 4 Adv Cache Optimization Technique II (Part 1)
Advanced Cache Optimization Technique II (Part 1) (00:32/17:43)
11:03 always available in the cache. The technique of bringing a block before it is demanded
11:10 is known as prefetching. So, when you do prefetching then we are trying
11:15 to improve the hits. You are trying to reduce miss rate as well as miss penalty. So, prefetch
11:24 items before processor request for them, what you do here? You fetch more blocks on a miss
11:31 you. Whenever there is a miss you bring the demanded block as well as a prefetch block.
11:37 So, how will you find out what is going to be a prefetch block?
11:41 We use prefetch engine or prefetch controller which looks into what is the pattern of memory
11:47 access; such that if there is an access to location l, we should be able to find out
11:54 l plus delta l, what is going to be the next location and prefetch that. And the most commonly
https://nptel.ac.in/courses/106103183

## Slide 5: 4 Adv Cache Optimization Technique II (Part 1)
Advanced Cache Optimization Technique II (Part 1) (00:32/17:43)
12:00 used method for prefetching is sequential prefetch; that means, if you bring block l,
12:05 then l plus 1 is also brought. Requested block is kept in I cache and the prefetch block
12:12 is kept in something known as stream buffer. So, stream buffer is an extra storage and
12:18 this extra storage is going to keep the prefetch block. So, whenever you get an address you
12:25 search in the cache memory in the instruction cache; if it is not available then look into
12:31 the stream buffer this. This can be considered as an extended version of your cache, where
12:37 you are keeping few more blocks of data in the cache memory. If a missed block is in
12:45 stream buffer then it is not like a cache miss; you are effectively having a cache miss,
12:51 but with of a lower penalty.
https://nptel.ac.in/courses/106103183

## Slide 6: 4 Adv Cache Optimization Technique II (Part 1)
Advanced Cache Optimization Technique II (Part 1) (00:32/17:43)
12:51 So, what we have in the prefetcher is like
12:57 processing engine is going to have a history recorder and then there is an aggressiveness
13:04 module which will find it out how much you have to prefetch; from where to prefetch and how many blocks you have to prefetch.
https://nptel.ac.in/courses/106103183
History recorder
Aggressiveness modle

## Slide 7: 4 Adv Cache Optimization Technique II (Part 1)
Advanced Cache Optimization Technique II (Part 1) (00:32/17:43)
13:08 And based upon that request is given prefetch
13:13 request is given to memory and the prefetch data is brought back.
13:18 So, prefetching is a technique by which a block is been brought to cache memory in advance
13:23 such that when it is really demanded; that will be having its presence in the l one cache
13:29 or its near vicinity. So, we call that extra structure which will store the prefetch data
13:35 is known as a stream buffer. We have seen that we could if you enable prefetching this
13:42 is somehow the benchmarks in SPEC 2000 suit, you could see that if you enable prefetching
13:49 the performance is improved across various benchmarks.
13:53 We can see that some of the applications like equake we are able to get performance close
13:59 to 1.9, where as some of the applications like fam 3D; we are getting only up to 1.18
https://nptel.ac.in/courses/106103183

## Slide 8: 4 Adv Cache Optimization Technique II (Part 1)
Advanced Cache Optimization Technique II (Part 1) (00:32/17:43)
14:08 times. Even though they all are improving performance certain applications will benefit
14:13 greatly from prefetching. These are characteristics of the memory footprint, some applications
14:19 are prefetch friendly where as some of them may not be prefetch friendly.
14:23 What we discussed just now is a hardware prefetching the other one we are going to discuss is prefetching
14:30 with the help of compiler. So, compiler is going to introduce certain instructions which
14:35 will tell that these instructions are going to be needed or these memory addresses are
14:40 needed in the near future so that should be prefetched. So, certain prefetch instructions
14:47 are added in the compiler code. So, prefetching will give performance only if processor read
14:53 from caches and execute while prefetching is in progress.
14:56 So, we can have two types of prefetching; one is called the register prefetch where
https://nptel.ac.in/courses/106103183

## Slide 9: 4 Adv Cache Optimization Technique II (Part 1)
Advanced Cache Optimization Technique II (Part 1) (00:32/17:43)
15:01 you loads a data into register, the other one is called cache prefetch where you load
15:07 the data into cache. This is a costly affair the register prefetch because we have very
15:12 few registers when your prefetch an existing data that is kept in the register has to be
15:16 flushed out; in the case of cache prefetch we have to make sure that the cache is not
15:21 polluted. So, using loop unrolling and scheduling for
15:27 prefetch data of adjacent iterations; let say you are going to work on an iteration
15:31 of loop ; when you work with the first iteration you know that the second iteration will also
https://nptel.ac.in/courses/106103183

## Slide 10: 4 Adv Cache Optimization Technique II (Part 1)
Advanced Cache Optimization Technique II (Part 1) (00:32/17:43)
15:38 be visited. For example, you work on a for loop which ranges from 1 to 10. When you work
15:43 on iteration 1; looking at the pattern the compiler should be able to tell that this
15:47 particular code is going to iterate from 1 to 10.
15:51 So, the data which is required for second iteration is prefetched when the first iteration
15:56 is in progress. Similarly, the data for the nth iteration is going to be prefetched when
16:04 n minus 1th iteration is in progress. In that way compiler is going to help the hardware
16:12 by prefetching data and instructions that is needed in the near future.
https://nptel.ac.in/courses/106103183

## Slide 11: 4 Adv Cache Optimization Technique II (Part 1)
Advanced Cache Optimization Technique II (Part 1) (00:32/17:43)
16:17 So, we have learnt few of the advanced cache optimization techniques;
the first one we
16:25 learned today was about write buffer merging. Whenever a write merging occurs or whenever
16:30 there is a write occurs, we look into the write buffer where to see whether there is
16:36 an entry for the same block in the past which is not a completely written in. So, in those
16:41 cases your step merge the entries to form one block and then we have learned about hardware
16:47 prefetching.
We have learned about compiler optimizations where in loop interchange in
16:53 the blocking techniques are been applied in order to get performance and the last one
16:58 is compiler assisted prefetching. So, with this we complete our basic optimizations
17:06 and advanced optimizations in cache memory. We will now work out few of the problems related
17:13 to cache memory which will give you a better grip on the on the topics.
https://nptel.ac.in/courses/106103183

## Slide 12: End