## Slide 1: 4 Adv Cache Optimization Technique I (Part 4)
Peter H. Chen

## Slide 2: 4 Adv Cache Optimization Technique I (Part 4)
Advanced Cache Optimization Technique I (Part 4) (00:32/40:09
30:00I can parallelly read some other blocks from bank 2 or bank 3.
30:05This will effectively increase the bandwidth of cache that is where we are trying to target.
30:10The amount of data that flows into the cache during a write operation or the data that
30:16flows out of the cache memory can be increased; if you use multi banked caches with multiple
30:22read or write ports.
30:23So, the idea is I can parallelly write into 2 different locations of my cache memory provided;
https://nptel.ac.in/courses/106103183

## Slide 3: 4 Adv Cache Optimization Technique I (Part 4)
Advanced Cache Optimization Technique I (Part 4) (00:32/40:09
30:30they are in different locations of cache now you try to learn some techniques which will
30:35reduce your miss penalty.
30:38Once its technique is known as early restart technique to reduce miss penalty; we know
30:42that once we encounter a miss we have to go to L2 cache bring a block of data this block
30:48of data means multiple words are there.
30:50Now, these blocks of data this one particular block of data cannot be transferred in a single
30:56stretch because your cache memory your L1 cache and L2 cache are connected by a bus.
https://nptel.ac.in/courses/106103183
Early restart:
as soon as the requested word arrives in the cache, send it to the processor and
then continue reading the rest of the block into the cache.

## Slide 4: 4 Adv Cache Optimization Technique I (Part 4)
Advanced Cache Optimization Technique I (Part 4) (00:32/40:09
31:02Let us say the bus width is 32 bits ready point of time only 4 bytes can be transferred
31:08together.
31:09So, if you have a bus which connects L1 and L2 cache by 32 bits, then only 4 bytes can
31:19flow from L2 to L1 in single stretch.
31:22If the block size happened to be 16 bytes; 16 bytes cannot travel together why?
https://nptel.ac.in/courses/106103183

## Slide 5: 4 Adv Cache Optimization Technique I (Part 4)
Advanced Cache Optimization Technique I (Part 4) (00:32/40:09
31:30Because the bus that connects your L2 cache memory and L1 cache memory can carry only
31:374 bytes at a time.
31:38So, you take first 4 bytes in the next cycle next 4 bytes again another 4 bytes and then
31:44the last 4 bytes.
31:45So, it requires 4 bus cycles to transfer your entire 16 bytes of data from L2 to L1.
31:54Now in the entire time your L1 cache is waiting for this 4 chunk 4 byte chunks to reach your
https://nptel.ac.in/courses/106103183

## Slide 6: 4 Adv Cache Optimization Technique I (Part 4)
Advanced Cache Optimization Technique I (Part 4) (00:32/40:09
32:03L1.
32:04Can I optimize this?
32:05This optimization is known as early restart technique.
32:08So, we do not your L1 cache controller do not wait for an entire block to be loaded
32:15for restarting CPU.
32:16So, CPU is now stalling you just assume a case that I cannot go for any other address.
32:20So, given an address it is a miss and cache controller has initiated activities in such
32:26a way that your L2 data is going to flow from L2 to L1 in multiple bus cycles.
https://nptel.ac.in/courses/106103183

## Slide 7: 4 Adv Cache Optimization Technique I (Part 4)
Advanced Cache Optimization Technique I (Part 4) (00:32/40:09
32:31We do not wait for the entire block to reach early restart means request words in order.
32:38So, you get; so you assume your word number 1, 2, 3, 4 is coming.
32:42So, you can assume that one word is what you can carry through the bus.
32:46So, in the given example there your block carries 4 words; one word will be coming second
32:54word, third word and fourth word.
32:55So, all the words are going to come from L2 to L1 in order word number 1, word number
https://nptel.ac.in/courses/106103183

## Slide 8: 4 Adv Cache Optimization Technique I (Part 4)
Advanced Cache Optimization Technique I (Part 4) (00:32/40:09
33:002, 3 and 4, but what happen is once the miss the word reaches L1 cache, forward it to the
33:09processor.
33:10So, L2 controller is not involved L2 controller will just return the data in order L1 controller
33:17has to understand word number 1 came put it inside the part of the block word number 2
33:21came again add up into your L1 block.
33:24Word number 3 let us say this will be the word that processer has as 4 directly give
https://nptel.ac.in/courses/106103183

## Slide 9: 4 Adv Cache Optimization Technique I (Part 4)
Advanced Cache Optimization Technique I (Part 4) (00:32/40:09
33:30it to processor; you put a copy in the L1 cache.
33:33Remember L1 cache block is not full still you require one more word to come.
33:41This can be illustrated with this diagram
33:43Consider the case there are 4 words that you needed processor is requesting for the third
33:49word.
33:50So, the block word number 1 as brought to the cache, word number 2 has brought, word
33:56number 3 has brought.
33:57As when 3 reaches, 3 is forwarded to your CPU and copying of word number 4 happens in
34:06background.
https://nptel.ac.in/courses/106103183

## Slide 10: 4 Adv Cache Optimization Technique I (Part 4)
Advanced Cache Optimization Technique I (Part 4) (00:32/40:09
34:07 So, we are not waiting entire for the entire cache block to be filled in between in transit;
34:13 whenever the requested word reaches you are going to forward them to the processor.
34:19 That is processor is going to get the word a little early cache block is going to restart
34:25 the processer, your cache memory controller is going to restart the processer a bit early
https://nptel.ac.in/courses/106103183

## Slide 11: 4 Adv Cache Optimization Technique I (Part 4)
Advanced Cache Optimization Technique I (Part 4) (00:32/40:09
34:31 that is what is known as early restart.
34:33 At another variation of this one is known as critical word first in the same previous
34:39 example we require third word of a block.
34:43 In the case of an early restart mechanism bring word number 1, 2, 3 is brought; 3 is
34:49 transfer to CPU then 4 is brought an background a bed more better optimization technique is
34:55 the critical word what CPU wants is being brought first.
34:59 So, request the missed word from memory first send it to processor as soon as it arrives
https://nptel.ac.in/courses/106103183

## Slide 12: 4 Adv Cache Optimization Technique I (Part 4)
Advanced Cache Optimization Technique I (Part 4) (00:32/40:09
35:05 and processor resume while the rest of the block is filled up the cache.
35:08 But here L2 cache controller also has to be involved; normal process is whenever CPU gives
35:14 the request if it is a miss L1 cache controller tells I use to I want this particular block
35:18 of data, the L2 cache controller will send word by word in order.
35:23 But when it comes to critical word first the processor will tell I want this block; inside
35:28 this block this particular word is of my interest send it first.
https://nptel.ac.in/courses/106103183

## Slide 13: 4 Adv Cache Optimization Technique I (Part 4)
Advanced Cache Optimization Technique I (Part 4) (00:32/40:09
35:32 So, word number n is send first then followed by the remaining words.
35:36 So, the L1 cache controller should rearrange the words of the block.
35:40 So, consider this case you have let us say third word is the requested 1.
35:45 So, first I bring 3 forward by the next one 4 it is cyclic.
35:50 Then I bring 1 and 2 as soon as 3 is brought it is forwarded to CPU.
35:56 So, 3 will reach L1 cache first and then I am forwarding it to the processor then comes
https://nptel.ac.in/courses/106103183

## Slide 14: 4 Adv Cache Optimization Technique I (Part 4)
Advanced Cache Optimization Technique I (Part 4) (00:32/40:09
36:02 4 then comes 1 and 2; this is continuing in a cyclic fashion.
36:05 So, the copying of 4, 1 and 2 is happening in the background.
36:10 So, this will effectively reduce miss penalty still further early restart and critical word
36:15 first or 2 techniques which are used to improve the miss penalty.
https://nptel.ac.in/courses/106103183

## Slide 15: 4 Adv Cache Optimization Technique I (Part 4)
Advanced Cache Optimization Technique I (Part 4) (36:20/40:09)
36:20 So, we will just summarize whatever is the techniques we have learned today.
36:24 We were continuing in our discussions with optimization principles in cache memory.
36:31 Small and simple level caches are used to improve the hit time;
lower the hit time lower will be the average memory access time.
36:42 Small caches and simple caches we reducing indexing time as well as hit or miss comparison time.
36:49 The second technique we were trying to use was to use way prediction;
predicting the way in which it is happening.
36:58 From past statistics, we are collecting information about most recently used to way and most frequently
37:05 used to way of a given set.
37:08 And from this we could find out where a current access whether based on prediction that way
37:15 can be preselected or not.
37:17 Preselected way is being now performing the tag comparison.
37:21 If it is a hit you get the benefit of a direct mapped cache; if it is hit then you go back
37:26 to the normal process of a set associative cache.
37:30 The third technique that we learned was about pipelined cache;
rather than considering cache as a single monolithic unit to divide the cache into sub operations like indexing, tag extraction, hit or miss comparison and data transfer; whereas, each one can happen in the clock cycle get into shorter clock cycle time.
https://nptel.ac.in/courses/106103183

## Slide 16: 4 Adv Cache Optimization Technique I (Part 4)
Advanced Cache Optimization Technique I (Part 4) (00:32/40:09
37:53 Then we learned about multi banked caches; rather than considering cache as a single
37:58 unit we can divide the cache into multiple banks, where in each bank I can have simultaneous
38:04 accesses.
38:05 We just discussed about non-blocking cache where whenever a miss is under progress we
38:11 call it as an outstanding miss; still processor can service the incoming request, it is called
38:17 hit under miss and hit under multiple misses.
38:20 Then we saw two techniques which will reduce miss penalty the first one is called early
38:26 restart technique; a block of data is brought as multiple words one after another from your
38:34 As and when the requested word reaches the L1 cache controller it is forwarding it to
38:38 the processor such that processor can be restart from the stall, a bit early.
38:44 The other technique which as slight modification of this rather than bringing all the words
38:48 from L2 cache to L1 cache in order; we bring the requested word first and then all others
38:55 are brought in their sequence.
38:57 So, these techniques whatever we discussed are trying to improve the optimization of
39:04 cache or we are effectively trying to reduce average memory access time.
39:08 There are few more techniques that we need to explore and these techniques we will discuss
39:14 in the next lecture.
https://nptel.ac.in/courses/106103183

## Slide 17: 4 Adv Cache Optimization Technique I (Part 4)
Advanced Cache Optimization Technique I (Part 4) (00:32/40:09)
39:16 So, kindly practice as many number of questions which are given in the textbook we are uploading
39:22 tutorial sheets as well go through them and make yourself comfortable in how much performance
39:29 gain you are able to see by playing around with these three numbers is hit time, miss
39:35 rate and miss penalty.
39:36 So, with this we conclude our today’s discussion; we will continue with cache optimization in
39:42 the next day.
https://nptel.ac.in/courses/106103183

## Slide 18: End