## Slide 1: 4 Adv Cache Optimization Technique I (Part 3)
Peter H. Chen

## Slide 2: 4 Adv Cache Optimization Technique I (Part 3)
Advanced Cache Optimization Technique I (Part 3) (00:32/40:09)
20:01then transfer of data.
20:03Let us say you are going to take 250 picoseconds for indexing, 250 picoseconds for reading
20:08the tag from the index location, 250 picoseconds for hit or miss comparison essentially your
20:14tag comparison and determine the 250 nano seconds for picoseconds for that are transfer.
20:19So, this makes that I can work the whole cache in a pipelined structure or pipeline frequency
20:25time of 250 picoseconds.
20:28So, every 250 picoseconds; I can get a new address now this address will be splited up
https://nptel.ac.in/courses/106103183

## Slide 3: 4 Adv Cache Optimization Technique I (Part 3)
Advanced Cache Optimization Technique I (Part 3) (00:32/40:09)
20:35into your tag index and the offset it takes one 250 picoseconds that is a one clock cycle
20:42to perform indexing.
20:43It takes another clock cycle to extract the tag it takes another clock cycle to perform
20:48hit or miss comparison and one more clock cycle to return the data.
20:52So, after giving an address only at the end of the fourth clock cycle I may be able to
20:57return the data.
20:58So, pipeline caches will surely access will be able to improve your bandwidth that is
https://nptel.ac.in/courses/106103183

## Slide 4: 4 Adv Cache Optimization Technique I (Part 3)
Advanced Cache Optimization Technique I (Part 3) (00:32/40:09)
21:03one point.
21:04Like in Pentium 4 let us core i7 you are where typically using 4 cycles for accessing cache
21:12memory.
21:13The problem with pipeline cache is you will come to know it is a miss only at a point
21:19hit or miss check.
21:20So, the moment you come to know it is a miss already 2 cycles are over.
21:24Because out 4 cycles in the third clock cycle only you will come to know whether it is a
21:29miss or not once you come to know its a miss then only I can take appropriate actions.
https://nptel.ac.in/courses/106103183

## Slide 5: 4 Adv Cache Optimization Technique I (Part 3)
Advanced Cache Optimization Technique I (Part 3) (00:32/40:09)
21:35So, misses will be relatively slow and usually increase branch mis prediction penalty as
21:42well.
21:43Now; what you mean by the concept of branch miss prediction penalty?
21:45We have learned that tackle control hazards when a control hazard is happening when you
21:51are executing an instruction whose outcome will tell you whether I should fetch the next
21:56instruction or I should fetch a distant instruction a target instruction.
https://nptel.ac.in/courses/106103183
In CPU design, hazards are problems with the instruction pipeline in CPU microarchitectures when the next instruction cannot execute in the following clock cycle, and can potentially lead to incorrect computation results.
Three common types of hazards are
1. data hazards,
2. structural hazards, and
3. control hazards (branching hazards).
There are several methods used to deal with hazards, including
1. pipeline stalls/pipeline bubbling,
2. operand forwarding, and
3. in the case of out-of-order execution, the score boarding method and the Tomasulo algorithm.

## Slide 6: 4 Adv Cache Optimization Technique I (Part 3)
Advanced Cache Optimization Technique I (Part 3) (00:32/40:09)
22:01So, we are using branch prediction algorithms and sometimes if the branch’s prediction
22:07happens to be wrong then it incur a penalty.
22:09So, the later you come to know whether it is a hit or a miss branch miss prediction
22:15also will have its own impact.
22:18This is easier for us to increase associativity because even if you increase associativity;
22:23since it is pipelined cache newer addresses are coming one after another and it parallely,
22:28you are still working on hit or miss comparisons of previously obtained addresses.
https://nptel.ac.in/courses/106103183

## Slide 7: 4 Adv Cache Optimization Technique I (Part 3)
Advanced Cache Optimization Technique I (Part 3) (00:32/40:09)
22:33Next concept is non-blocking cache; consider a scenario where CPU is giving going to give
22:39an address.
22:40This address has to be looked into cache let us say it turned out to be a miss what is
22:45the next course of action?
22:46We have to facilitate necessary mechanism such that you go into L 2 cache and bring
22:54the block of data.
22:55Transferring of data from L2 cache look up of L2.
22:59L2 look up means to know whether it is a hit or a miss and transferring the data from L2
https://nptel.ac.in/courses/106103183

## Slide 8: 4 Adv Cache Optimization Technique I (Part 3)
Advanced Cache Optimization Technique I (Part 3) (00:32/40:09)
23:04to L1 We will take some amount of time few clock cycles it will take; what will the processor
23:09do during this time?
23:10Or to rephrase the question in an another way once I come to know it is a miss in L1
23:17cache L2 look up is in progress will the processor be stalling.
23:21Yes, processor will be stalling when you incur a miss. can I help the processor?
23:26yes cache memory can help the processor anyway I have already began necessary steps in order
https://nptel.ac.in/courses/106103183

## Slide 9: 4 Adv Cache Optimization Technique I (Part 3)
Advanced Cache Optimization Technique I (Part 3) (00:32/40:09)
23:32to bring a block of data from L2 cache.
23:36In the meantime, processor can still give address to L1 and L1 can support them or can
23:45they cache control or still accepts memory request from processor; when it is already
23:51processing miss on L1.
23:55So, caches can serve hits under multiple cache misses in progress.
23:59So, one concept that I would like to introduce here is known as hit under a miss.
24:06So, what you mean by hit under miss?
24:09When a miss is in progress the actions that are to be done when I encounter a miss when
https://nptel.ac.in/courses/106103183
A non-blocking cache is a type of cache that can service multiple memory requests at the same time.
In contrast, a blocking cache can only serve one request a time.

## Slide 10: 4 Adv Cache Optimization Technique I (Part 3)
Advanced Cache Optimization Technique I (Part 3) (00:32/40:09)
24:16it is in progress; can I service hits?
24:20That is called a hit under miss.
24:24Another property is known as hit under multiple misses what you mean by hit under multiple
24:28miss?
24:29Already I encountered a miss.
https://nptel.ac.in/courses/106103183

## Slide 11: 4 Adv Cache Optimization Technique I (Part 3)
Advanced Cache Optimization Technique I (Part 3) (00:32/40:09
24:31So, I am in the process of bringing the block since I am a non blocking cache one more address
24:36is coming that also happen to be a miss.
24:39So, that also is in progress; so hit under now 2 miss.
24:43So, can I still service hits?
24:45So, hit under 2 miss hit under 4 miss means I can have 4 outstanding misses currently
24:51in progress still I can service the hit.
24:54under 16 miss, hit under 64 miss.
24:58So, once I get the block back how will I know which block is this whether it is part of
https://nptel.ac.in/courses/106103183

## Slide 12: 4 Adv Cache Optimization Technique I (Part 3)
Advanced Cache Optimization Technique I (Part 3) (00:32/40:09
25:02miss number 1, miss number 2, miss number 3 and on.
25:06So, this particular diagram is going to give you a bit of idea regarding this.
25:11You are having a miss that is happening at this point; the miss penalty already started,
25:19but CPU is still giving you addresses; that means, I can still service a hit my miss is
25:26under progress and still I could service the hit; later I got one more miss and that is
https://nptel.ac.in/courses/106103183
Multiple outstanding misses

## Slide 13: 4 Adv Cache Optimization Technique I (Part 3)
Advanced Cache Optimization Technique I (Part 3) (00:32/40:09
25:31also been process.
25:32So, the miss penalty for that miss starts and then I came to a point where I got one
25:37more miss that happens and beyond which I cannot do.
25:40So, it is basically multiple outstanding misses that are going to help in this scenario.
25:47So, this is basically known as hit under multiple misses.
25:52So, the typically need an Out Of Order superscalar processor for IPC increase.
25:59So, when you have a non blocking cache?
https://nptel.ac.in/courses/106103183

## Slide 14: 4 Adv Cache Optimization Technique I (Part 3)
Advanced Cache Optimization Technique I (Part 3) (00:32/40:09
26:01When you have a processor that can run out of order it is a current instruction is encountering
26:06a miss let us say the adjacent instruction is not dependent on the current instruction;
26:10where can I go and fetch the next instruction provided the next instruction is there in
26:16cache memory.
26:17So, we require processors there is an extra feature that the processor should support
26:21that is known as out of order; superscalar processors which can run adjacent instruction
26:27it is the current instruction is encountering with a miss
https://nptel.ac.in/courses/106103183
In computer engineering, out-of-order execution (or more formally dynamic execution) is a paradigm used in most high-performance central processing units to make use of instruction cycles that would otherwise be wasted.
In this paradigm, a processor executes instructions in an order governed by the availability of input data and execution units, rather than by their original order in a program.
In doing so, the processor can avoid being idle while waiting for the preceding instruction to complete and can, in the meantime, process the next instructions that are able to run immediately and independently.

## Slide 15: 4 Adv Cache Optimization Technique I (Part 3)
Advanced Cache Optimization Technique I (Part 3) (00:32/40:09
26:30So, the L2 here actually supported with L1 MSHR.
26:34So, in order to keep track of which of the misses are currently going to be returned;
26:39we need to understand what is the data, that is coming from L2.
26:44And once the data reaches L1 there is a book keeping mechanism and is book keeping mechanism;
26:49which is known as MSHRs- Miss Service Handling Registers, they actually work it out.
26:54So, on an L1 miss you are going to allocate in MSHR entry.
26:59So, once they request let us say this is entry number 1, when they reply comes back I come
https://nptel.ac.in/courses/106103183

## Slide 16: 4 Adv Cache Optimization Technique I (Part 3)
Advanced Cache Optimization Technique I (Part 3) (00:32/40:09
27:05to know this is the reply for 1.
27:07So, 1 is being entered and it is being deleted; so, MSHR entry 16 means processor can have
27:1416 outstanding misses on this cache controller or the cache control of will permit 16 outstanding
27:19misses.
27:20When the 17th request is coming if it is a miss it is not allowed.
27:23So, once you have 16 outstanding misses already in transit, I cannot further accept anymore
27:28request.
27:29So, that is called hit under 16 misses.
https://nptel.ac.in/courses/106103183

## Slide 17: 4 Adv Cache Optimization Technique I (Part 3)
Advanced Cache Optimization Technique I (Part 3) (00:32/40:09
27:32Now, one of the important feature of L1 cache non blocking caches is processor can hide
27:38L1 miss penalty.
27:40Since I am using L1 caches are non blocking; it reduces the effective miss penalty by overlapping
27:46misses I have my miss number 1 in transit, but processor is not waiting it is not stalled
27:51it gives a next address let us say that is a hit processor is working 3, 4, 5, 6 many
27:57addresses are be returned they are all hits.
https://nptel.ac.in/courses/106103183

## Slide 18: 4 Adv Cache Optimization Technique I (Part 3)
Advanced Cache Optimization Technique I (Part 3) (00:32/40:09
28:00Address number 8 it can be miss, but still processor is not stalling it is in transit
28:06because of the MSHR principle non blocking cache.
28:09So, effectively even though we have latencies for the cache misses; they are not encounter
28:15as a stall as for as the processer is concerned.
28:18Next optimization is called multi banked cache; multi banked caches are used to increase the
28:26cache a bandwidth.
28:27So, rather than considering your cache as single unit which is kept in one place, where
https://nptel.ac.in/courses/106103183
A single cache bank is replicated several times to form a multi-bank cache.
Banks are interleaved in the memory space (at cache line granularity), therefore each address is unequivocally mapped on specific bank, and globally the multi- bank cache covers the entire L3 space.

## Slide 19: 4 Adv Cache Optimization Technique I (Part 3)
Advanced Cache Optimization Technique I (Part 3) (00:32/40:09
28:32processor will come and access, why cannot I divide my caches into multiple fragments,
28:38segments and access can be permitted to be segments in parallel.
28:43So, rather than having single monolithic block divide the cache into independent banks which
28:49will support simultaneous access.
28:51ARM cortex support up to 4 banks.
28:56 Intel i7 support 4 banks for L1 and 8 banks for L2.
https://nptel.ac.in/courses/106103183

## Slide 20: 4 Adv Cache Optimization Technique I (Part 3)
Advanced Cache Optimization Technique I (Part 3) (00:32/40:09
29:02And typically the method that is used in all these multi banked cache is called sequential
29:08interleaving.
29:09Consider this case where you have a cache memory that is having 16 blocks.
29:16Now, these 16 blocks are scattered across 4 banks namely bank 0, bank 1, bank 2 and
29:24bank 3. where block number 0 is part of bank 0.
29:27Block number 1 rather than storing in bank 0 which is stored in bank number 1; so 2 is
https://nptel.ac.in/courses/106103183
16

## Slide 21: 4 Adv Cache Optimization Technique I (Part 3)
Advanced Cache Optimization Technique I (Part 3) (00:32/40:09
29:32here 3 is here again 4 is here 5, 6, 7 like this.
29:37So, when we are already processing in bank 0 we know that the adjacent block is not kept
29:43in bank 0 it is kept in bank 1; you can do all the pre work that is required.
29:48So, once the task in bank 0 is over I can return data from bank 1 or if I have multiple
29:54read write ports into the cache memory whenever I am reading bank 0; some blocks in bank 0,
https://nptel.ac.in/courses/106103183

## Slide 22: End